## Slide 1: Way forward on beam declaration principles
R4-161374, Ericsson,…

## Slide 2: WF on beam declaration principles
The minimum set of beams to declare for conformance are as follows:
  narrowest intended BWθ, narrowest intended BWϕ (possible when narrowest intended BWθ) at the reference beam direction
  narrowest intended BWϕ, narrowest intended BWθ (possible when narrowest intended BWϕ) at the reference beam direction
  Widest intended BWθ , widest intended BWϕ (possible when widest intended BWθ) at the reference beam direction
  Widest intended BWϕ – widest intended BWθ (possible when widest intended BWϕ) at the reference beam direction
  BWθ and BWϕ which provide highest intended EIRP of all possible beams at the reference beam direction.
  Some of these beams may be the same, in which case fewer than 5 beams will be declared and tested

## Slide 3: WF on beam declaration principles
The beams that are declared are the ones with the max intended EIRP for any individual beam with the applicable beam width.
It may be that for a given beamwidth, several beams at maximum intended individual beam EIRP can be transmitted. Such beams must have independent RF power resources from one another.
  Independent power resources means that the beams are transmitted from different transmitters (although the specification may not mention transmitters)
For each declared BeamWidth If there are parallel beams with independent RF power resources then the number of them shall be declared

## Slide 4: WF on beam declaration principles
For conformance testing, declared beams are tested individually
  In case for a given beamwidth more than one beam can be transmitted with maximum individual beam EIRP, it is FFS whether all beams that can be produced in parallel should be tested (one at a time)
With the above WF, a simple test model should be used (preferably (E)TM1.1 unless there is any other issue with that TM)