## Slide 1: 3GPP TSG-RAN WG4 Meeting #78 R4-161379 St. Julian’s, Malta, 15 – 19 February, 2016
Way Forward with eMTC MPR
Qualcomm, Ericsson, Nokia Networks, Sony, NTT Docomo, Intel, Verizon

## Slide 2: Background
Emission requireements were agreed in RAN4#77 AH NB-IoT in [1] and companies were encouraged to submit simulation results on eMTC MPR
This WF summarises MPR from
  R4-160640 Ericsson
  R4-160117 Qualcomm
  R4-160878 Sony
  R4-160685 Nokia

## Slide 3: Background
The endrosed CR from RAN4#78 (R4-158447) included MPR for 1.4 MHz system BW
All the data and analysis indicates that MPR for 3 MHz system BW is equal or even more than 1.4 MHz.
After discussions the data taken from all contributions was considered and MPR tables in following table were agreed

## Slide 4: Proposal: MPR tables
Modulation | Channel bandwidth / Transmission bandwidth (NRB) |  |  |  |  |  | MPR (dB)
 | 1.4 | 3 | 5 | 10 | 15 | 20 | 
 | MHz | MHz | MHz | MHz | MHz | MHz | 
QPSK | >2 | >2 | >3 | >5 | - | - | ≤ 1
QPSK | >5 | >5 | - | - | - | - | ≤ 2
16 QAM | ≤2 | ≤2 | >3 | >5 | - | - | ≤ 1
16QAM | >2 | >2 | >5 | - | - | - | ≤ 2
Modulation | Channel bandwidth / Transmission bandwidth (NRB) |  |  |  |  |  | MPR (dB)
 | 1.4 MHz | 3.0 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 
QPSK | >2 | >2 | >1 | >4 | - | - | ≤ 1
QPSK | >5 | >5 | - | - | - | - | ≤ 2
16 QAM | ≤ 2 | ≤ 2 | >1 | >3 | - | - | ≤ 1
16QAM | >2 | >2 | >3 | >5 | - | - | ≤ 2
PC3
PC5