## Slide 1: WF on MIMO OTA
Vodafone, AT&T, Telecom Italia, NTT Docomo, SoftBank, Deutsche Telekom, TeliaSonera, Rogers Communications, T-Mobile USA, China Mobile, Sprint, Dish, Intel
Malta, 15 – 19 Feb, 2016 R4-161406
Approval

## Slide 2: Background (1/3)
MIMO OTA WI has evaluated the candidate methods towards concluding on whether harmonization is successful or not
Lab testing and associated analysis of results have been conducted considering 4 methodologies (RC, RC+CE, MPAC and RTS) where RC is Reverberation Chamber, RC+CE is Reverberation Chamber+Channel Emulator, MPAC is MultiProbe Anechoic Chamber and RTS is Radiated Two Stage
Latest MIMO OTA WI has been extended several times from June’15, Sept’15, Dec’15 and Mar’16. And RAN4#78 is the last meeting where a decision on harmonization has to be made
Harmonization phase has completed with only 3 devices per channel model and band, and only 3 bands being considered
Additionally 4 more devices have been added in the last phase of harmonization for estimating “b”, which turned the group to recalculate harmonization
Residual errors have been only optimized for 70%, not 95%
RTS cannot test TDD devices as of today and requires support from UE side

## Slide 3: Background (2/3)
Harmonization cost has been calculated among the options for harmonization. Cost has been calculated as C=Max(h_B7,h_B13,h_B41)-m_MPAC
Color code has been applied (<1dBgreen, >=1dB&<2dByellow, >=2dBred) for visualization purposes
From this, Harmonization potential can be observed
Cost | RC&MPAC | RC+CE&MPAC | RTS&MPAC | RC+CE&RTS&MPAC | RC&RC+CE&RTS&MPAC
C | 1,6 | 1,6 | 0,5 | 1,6 | 1,6
D | 1,8 | 1,8 | 0,7 | 1,8 | 1,9
G (3 orientations) | 4,5 | 2,0 | 1,0 | 2,0 | 4,5
G (2 orientations- P45, L45) | 4,9 | 2,3 | 1,2 | 2,3 | 4,9
G (1 orientation, all 3 combinations) | 5,5 | 3,2 | 2,3 | 4,0 | 6,6
H (3 orientations) | 4,4 | 2,0 | 1,2 | 2,0 | 4,4
I | 2,0 | 1,8 | 1,0 | 1,8 | 2,0
J | 1,9 | 1,9 | 1,2 | 1,9 | 1,9
 | note: RTS cannot test TDD (as of today) and requires UE support |  |  |  | 

## Slide 4: Background (3/3)
Additionally, as offsets were optimized for 70%, check is made at 95% to see if residuals (“r”) increase or not
This check is made so that we make sure that harmonization also holds for 95% throughput KPI
Colour code applied here is: (<0.5green, >=0.5 red) for visualization purposes
Note again RTS cannot test TDD band (as of today) and so Band 41 check could not be performed (yet marked green)
check 70%&95% | RC&MPAC | RC+CE&MPAC | RTS&MPAC | RC+CE&RTS&MPAC | RC&RC+CE&RTS&MPAC
C | 1,9 | 0,0 | 0,0 | 0,0 | 1,4
D | 2,1 | 0,1 | 0,4 | 0,1 | 1,6
G (3 orientations) | 1,9 | 0,1 | 0,2 | 0,1 | 1,7
G (2 orientations) | 2,5 | -0,2 | 0,0 | -0,3 | 1,8
H (3 orientations) | 1,7 | 0,1 | 0,1 | 0,1 | 1,7
I | 1,9 | -0,1 | 0,2 | -0,1 | 1,7
J | 1,8 | -0,1 | 0,2 | -0,1 | 1,7

## Slide 5: Agreements (1/2)
Final harmonization cannot be successfully claimed. But potential for harmonization can be found. In this situation, a single method shall be selected according to WID, while work on improving harmonization is deemed possible and needed
Select MPAC methodology, and start new activity on performance requirement phase for MPAC
Select UMi channel model, and inverse averaging. Option C
Select the following KPIs: 70% and 95%
How to treat failing of devices:
  For 95% tput: 2 orientations/azimuth rotations that fail are allowed. If more orientations fail then device fails test
  For 70% tput: 1 orientation /azimuth rotations that fail is allowed. If more orientations fail then device fails test
Start follow-up harmonization activity in parallel to Performance requirement activity above, for the pair or pairs of methods that have potential harmonization
  This follow-up activity will test as many devices as MPAC activity with the aim to augment and improve harmonization
  This follow-up activity will also increase the bands to be considered for harmonization
  Add UMa only option (Option J) for harmonization it in this follow-up harmonization activity which will be tested in parallel to Umi harmonization
Next slide: methods that have shown potential for harmonization are identified

## Slide 6: Agreements (2/2)
Due to robustness check at 95%, methods involving RC-only shall not be considered
RC+CE&MPAC, RTS&MPAC and RC+CE&RTS&MPAC shall be considered in the harmonization activity
Everything can be done in the same WI
Bands for performance requirement definition activity: 1,2,3,4,5,7, 8,12,13,19,20,28,32,38,40,41,42,46
The first set of bands to define requirements for and to perform harmonization activity are 2 FDD low bands, 2 FDD high bands and 2 TDD bands
if harmonization fails for a particular set of corresponding channel models, then that method is not applicable for testing in that particular set of corresponding channel model
Cost of harmonization | RC&MPAC | RC+CE&MPAC | RTS&MPAC | RC+CE&RTS&MPAC | RC&RC+CE&RTS&MPAC
C | 1,6 | 1,6 | 0,5 | 1,6 | 1,6
Residual delta between 70% & 95% | RC&MPAC | RC+CE&MPAC | RTS&MPAC | RC+CE&RTS&MPAC | RC&RC+CE&RTS&MPAC
C | 1,9 | 0,0 | 0,0 | 0,0 | 1,4

## Slide 7: Agreements (3/3)
Sample size for performance requirement: 100 measurements as a minimum
How to claim new harmonization activity is successful
  Same bands (or set) as in the performance activity will be addressed in the same order, and harmonization will be checked after the performance requirement for each band (or set) is finalized.
  How many measurements samples per band: 30 of devices used for Performance requirement phase will be used for this harmonization activity. And tested in the same lab to minimize Mus with a controlled environment

## Slide 8: Open items
Study how to perform averaging across orientations that did not fail the KPI
Add Rayleigh validation
Add how to extend the concept of devices failing in MPAC as agreed in slide 5 to RC+CE method
Think what happens if we don’t find a single lab with a controllable environment
Include statistical analysis to determine when to stop testing more devices for harmonization
Study how to find the offset
Study the distribution of residuals when analysing the cost
Study how to calculate the cost and threshold