## Slide 1: WF on eD2D RRM
Qualcomm, Intel, Nokia Networks, Alcatel-Lucent
R4-161421
3GPP TSG-RAN WG4 Meeting #78
Malta, Feb 15th – Feb 19th, 2016

## Slide 2: Multicarrier D2D operation: Remaining aspects
Proposal 1: For Discovery when no request for Gaps (for discovery) is signaled by UE, interruptions allowed:
  For discovery on serving cell (PCell/SCell)
    Extend existing Rel-12 interruptions to PCell and any activated Scell
    For discovery period is less than 320ms, the interruption rate is additionally limited to 0.625%.
  For discovery on non-serving carrier, then the UE is allowed interruptions:
    With up to missed ACK/NACK probability of min(0.5%, 3*2/T_discovery(ms)*100%)
Proposal 2: For communications on non-serving carrier and Pcell is not broadcasting SIB18, interruptions allowed:
  With up to 0.5% missed ACK/NACK probability
Proposal 3: It is FFS if any restriction on the number of non-serving ProSe carriers need to be clarified in TS 36.133.
  Note: Does not affect closing of WI.

## Slide 3: Inter-frequency D2D Discovery: Remaining aspects
Proposal 1: Only the following interruptions allowed when Gaps are configured
  UL interruption allowed on a subframe configured as reception gap by the eNodeB only if the subframe immediately preceding / immediately following is not configured as a reception gap.
  Additionally, if D2D is on a non-serving FDD carrier and that carrier is used for D2D synchronization, UE is allowed to interrupt 1 subframe in a discovery period.
    Note: The subframe interrupted must be within the reception gap configured by the eNodeB.
  Additionally, if D2D Tx is on a carrier that is not configured for UL, UL/DL interruption allowed on 2 subframe for each discovery / SLSS transmission configured for the UE.
    Note: The subframes interrupted must be within the transmission gap configured by the eNodeB.

## Slide 4: Inter-frequency D2D: Remaining aspects (Cont’d)
This slide is for information only.
Example of interruptions when Gaps are configured

## Slide 5: Inter-frequency D2D: Remaining aspects (Cont’d)
Proposal 2: Cell reselection requirements on non-serving carrier
  Apply when all parameters for cell (re)selection are provided by serving cell
  Tdetect, Tmeasure, Tevaluate for cell reselection to intra-frequency cells:
  UE to evaluate S-criterion of the selected reference cell every discovery period
Discovery period [s] | Tdetect,EUTRAN_ProSe_Intra (number of discovery periods) | Tmeasure,EUTRAN_ProSe_Intra (number of discovery periods) | Tevaluate,E-UTRAN_ProSe_intra (number of discovery periods)
Discovery period<=0.32 | (36) | (4) | (16)
0.32<Discovery period<=0.64 | (28) | (2) | (8)
0.64<Discovery period<=1.28 | (25) | (1) | (5)
1.28<Discovery period<=10.24 | (23) | (1) | (3)

## Slide 6: OOC discovery
Proposal 1: Interruptions requirements when OOC on D2D carrier, while having a serving cell on a non-D2D carrier, are the same as multicarrier D2D operation with D2D on non-serving carrier
Proposal 2: Gaps are allowed for shared Tx chain for PS use.

## Slide 7: UE-NW relays
Proposal 1: For relay selection/reselection, the following requirements are proposed for Tmeasure and Tevaluate:
  This requirement are applicable for selection/reselection to a relay that is transmitting PSDCH within the discovery resource pool as configured for the remote UE, and follows a synchronization source that either the same or is synchronized to the one use by remote UE.
Proposal 2: If remote UE has selected a relay UE, then it shall measure SD-RSRP of the selected relay UE every Tmeasure period.
Proposal 3: Each measurement for SD-RSRP is based on averaging over the retransmissions within 1 discovery period.
Discovery Period [s] | Tmeasure,ProSe_Relay_Intra [s] (number of discovery periods) | Tevaluate, ProSe_Relay_intra [s] (number of discovery periods)
0.04≤Discovery period≤10.24 | Note 1 (4) | Note 1 (16)
NOTE 1: Time depends upon the configured Discovery period. |  |