## Slide 1: Problems and Possible Way Forward on bandwidths for CA including B41 and B42
3GPP TSG-RAN WG4 Meeting #78 R4-161464
St. Julian’s, Malta, 15 – 19 Feb, 2016
Agenda item: 6.16.2.3 (REL-13)
Source: SoftBank Corp.
Document for: Approval

## Slide 2: Observation: REL-13 (36.101 v13.2.1)
B41 is supported in CA as 10, 15 and 20MHz or their combinations.
  CA_41C supports 5MHz BW only in BCS1 but this is not linked to xA-41C (it refers to BCS0: no 5MHz in B41)
On the other hand, Band 42 supports 5MHz BW in all BCSs
Moreover, 41A-42A does not support 5M+5M
There might be a contradiction: 41A-42C with 5MHz B42 cannot fall back to 41A-42A as there is no 5MHz in B42

## Slide 3: (a)Problem in REL-13
The fundamental problem is in inconsistencies among 41-42 2CA and 3/4 CAs in terms of support of 5MHz BW in B42
So fallback is “broken” when (and only when) the 3CA/4CA above uses 5MHz in B42.
We need to settle this issue.
 |  | Rel | 5MHz in B42? | 
2CA | 41A-42A | 12 | No | 
3CA | 41A-42C | 13 | Yes | 
 | 41C-42A | 13 | Yes | 
4CA | 41C-42C | 13 | Yes | 

## Slide 4: (b)R4-160603: B3+B41+B42 (36.101 v13.2.1)
 | Band | 5MHz | 10MHz | 15MHz | 20MHz
B3+B41 | 3 | Yes | Yes | Yes | Yes
 | 41 | Yes | Yes | Yes | Yes
B3+B42 | 3 | Yes | Yes | Yes | Yes
 | 42 | Yes | Yes | Yes | Yes
B41+B42 | 41 | No | Yes | Yes | Yes
 | 42 | No | Yes | Yes | Yes
B3+B41+B42 | 3 | Yes | Yes | Yes | Yes
 | 41 | Yes->No | Yes | Yes | Yes
 | 42 | Yes->No | Yes | Yes | Yes
41A-42A does not support 5M+5M in the latest version of 36.101
So 3A-41A-42A (or any CA including 41A-42A)should not include 5M+5M in B41+B42 portion from the standpoint of consistent fall-back: it is to align with WID but reservation is put when we decide to add 5MHz to B41+B42

## Slide 5: Possible Way Forward on “5MHz in B42”
For REL-13 and before, there are two choices (while we should also take care of R4-160603):
1) Leave them as they are (some fall backs are denied)
  It seems that 5MHz in B42 is rarely used in China/Japan then the problem in real operation would not be serious.
  But this is against a rule: “A terminal which supports a DL CA configuration shall support all the lower order fallback DL CA combinations and it shall support at least one bandwidth combination set for each of the constituent lower order DL combinations containing all the bandwidths specified within each specific combination set of the upper order DL combination.”
2) Remove 5MHz BW of B42 from B41+B42 CA to guarantee consistent fall-backs
  Delete 5MHz from all the B41+B42 CA BWs: 41A-42C, 41C-42A and 41C-42C
  Impacts for approved/finished WIDs => Done with “correction”(TEI-13) or do we need RAN-P approval (i.e. BW is managed in WID)?
  As a matter of constructing table: we need to define a new BCS set(BCS1) for 42C which does not include 5MHz BW to define 41A-42C or 41C-42C

## Slide 6: Possible Way Forward on “5MHz in B42”
For REL-14 WIDs : 1A(3A)-41C-42C
Change the WIDs according to the decisions above (Upon approval of R4-160603, we need to remove 5MHz in B41)
  Anyway, we need check consistency around CAs including B41 and B42 : basically B41 BW should be ≥ 10MHz.