## Slide 1: WF on BS demod performance for new PUCCH formats
Nokia
R4-162484
3GPP TSG-RAN WG4 Meeting #78bis
San Jose del Cabo, Mexico, April 11 – 15, 2016
Agenda Item: 6.11.3

## Slide 2: Proposals
Use SNR to achieve 1% BLER as the performance metric for the BS demod requirements for new PUCCH formats.
BS demod requirements are only defined for PF4 in Rel-13.
RAN4 should decide in RAN4#78bis whether to define BS demod requirements for 128bits in Rel-13.
  Assumptions for the performance tests are in the next slide.
  Interested companies are encouraged to provide simulation results with implementation margins for RAN4#79.

## Slide 3: simulation assumptions
Codeword selection | Random selection for both HARQ-ACK and P-CSI
Codebooks | [Semi-static (codebooksizeDetermination-r13=1)]
ACK repetitions | Disabled
Propagation conditions | EPA5, EVA70 Propagation channel definitions to be reused from 36.104.
Cyclic Prefix | Normal CP
Channel BWs | 10, 15, 20MHz
Carrier definition | Carrier frequency: 2.0 GHz PUCCH on PCell (single PUCCH group) Number of PRBs for PF 4: 1 PRB for 24 and 48bits, 2PRB for 128bit
PUCCH multiplexing | 1 UE
Antenna’s configuration | UE: 1Tx BS: 2Rx, 4Rx, 8Rx correlation between branches is 0 no power imbalance between branches
Timing estimation | Perfect timing estimation
Frequency hopping | At slot boundary
Power control | Off