## Slide 1: WF on eD2D RRM test cases
Qualcomm, Samsung, Nokia
R4-162718
3GPP TSG-RAN WG4 Meeting #78bis
San Jose Del Cabo, MX, Apr. 11th – Apr. 15th, 2016

## Slide 2: eD2D RRM test case list
Proposal 1: RRM test cases and test coverage is proposed as follows
Test 1 | Title | Discovery Tx on non-serving cell
 | To verify | Cell reselection for discovery Tx on non-serving cell (7.16.4) Timing accuracy requirements for discovery Tx on non-serving cell (7.16.2.1.2)
 | Configuration | RRC-C DRX, FDD-FDD, AWGN, Discovery Tx trigger
Test 2 | Title | Interruptions during discovery reception on non-serving frequency
 | To verify | Interruptions during discovery with Gaps (non-serving) (7.16.3.4) Interruptions during discovery on non-serving carrier without Gaps (7.16.3.3)
 | Configuration | RRC-C, FDD-FDD, AWGN, Discovery Rx trigger
Test 3 (NOTE 1) | Title | Interruptions during discovery transmission on non-serving frequency
 | To verify | Interruptions during discovery with Gaps (non-serving) (7.16.3.4) Interruptions during discovery on non-serving carrier without Gaps (7.16.3.3)
 | Configuration | RRC-C, FDD-FDD, AWGN, Discovery Tx trigger
Test 4 (NOTE 3) | Title | Interruptions during discovery on Pcell with discovery period less than 320ms
 | To verify | Interruptions during discovery (7.16.3.3)
 | Configuration | RRC-C, FDD-FDD, AWGN, Discovery Rx trigger

## Slide 3: eD2D RRM test case list (Cont’d)
Proposal 1 Cont’d
NOTE 1: Test 3 is FFS based on company evaluation of test feasibility.
NOTE 2: FFS is additional test is needed for OOC scenario for selection/reselection of relay UE.
NOTE 3: FFS if additional (similar) test is needed with Pcell + Scell, with discovery on Pcell to verify interruptions to Pcell + Scell.
Proposal 2: Existing OOC tests with D2D communication configured are sufficient for OOC requirements, and UE need not be re-tested with D2D discovery
  NOTE: A UE that supports Rel-13 D2D communication also supports OOC D2D Discovery.
Test 5 | Title | Interruptions during communication on non-serving carrier
 | To verify | Interruptions during communication on non-serving carrier (7.16.3.5)
 | Configuration | RRC-C, FDD-FDD, AWGN, Communication Rx trigger, Serving cell not broadcasting SIB18
Test 6 (NOTE 2) | Title | Selection/Reselection of Relay UE
 | To verify | Selection/Reselection of Relay UE (Idle/Connected/OOC) (7.16.5, 11.7)
 | Configuration | RRC-C DRX, FFS if additionally test for OOC, FDD, AWGN, No trigger (signaling test)