## Slide 1: 3GPP TSG-RAN WG4 Meeting #78bis San Jose del Cabo, Mexico, 11th – 15th Apr 2016
Huawei, HiSilicon, Ericsson, Qualcomm, Intel, LG electronics
Way forward on demodulation performance and CSI requirements for LAA
R4-162753

## Slide 2: Background
RAN4#78 Malta meeting, WF R4-1611862 was agreed, but still many open issues left.
As per the further discussions in RAN4#78bis, progress was made as following slides.

## Slide 3: General
        Introduce new PDSCH tests in CA mode for Rel-13 LAA with
  1 PCell with 1.4MHz ~20MHz BW + 1 LAA SCell both with 20MHz BW;
  Both FDD PCell and TDD PCell should be covered;
  Both PCell and LAA SCell should be verified.
Full, Initial and end partial SF to be tested
  Option1: Full subframe
  Option2: [Initial paritial subframe] + full frame + ending partial subframe
        (e)PDCCH performance verification:
  Option 1: Explicitly
  Option 2: Implicitly verify the (e)PDCCH performance via PDSCH tests

## Slide 4: General
MBSFN subframe configuration
  Option1 : MBSFN subframe is not configured
  Option2: MBSFN subframe is configured for DMRS-based transmission mode
DRS configuration: with DMTC period 80ms

## Slide 5: General
Frequency offset and timing error, and synchronization:
  Frequency offset and timing error of LAA Scell should be set relative to Pcell
    [750]Hz, [30.26]μs
    200 Hz, 3 us
    Other options are not precluded.
  Note: The defer time due to slot duration mismatch with LTE basic time unit is FFS
    The above proposed time offset may be updated subjected to the discussion results of this issue
Reference receiver:
  MMSE-IRC receiver
    With practical frequency and timing tracking
    With practical detection

## Slide 6: PDSCH test cases and parameters
For PCell, to save the simulation efforts, the following existing test cases maybe used if needed
  TM3 rank-2, EVA70, 2x2 Low, 16QAM ½
  TM4 rank-2, EVA5, 4x2 Low, 16QAM ½
  TM3 rank-2, EVA70, 2x2 Low, 16QAM ½
For the LAA SCell
  Option 1: TM3 4x2, TM9 2x2(Qualcomm)
  Option 2: TM3 2x2, TM9 4x2(Intel and LGE, Qualcomm)
  Option 3: TM3 2x2, TM4 4x2, TM9 2x2 (Ericsson, Huawei)

## Slide 7: Test metric
  Reuse relative throughput (TP)
    70% TP as starting point.
    Relative throughput is the ratio of the throughput values per component carrier to the sum of the nominal maximum throughput values per component carrier.
      Nominal maximum throughput is
Nominal Max throughput = (Total data transmitted)/(Total time used for transmission)

## Slide 8: CSI test
CQI feedback mode:
  Aperiodic CQI test
  Periodic CQI test is FFS
One CSI test for CRS based transmission scheme and one CSI test for DMRS based transmission scheme for the corresponding CQI feedback mode
Transmission mode
  Baseline: TM3 (CRS based CSI measurement) and TM9 (CSI-RS based)
    If any issues is identified for TM3, TM2 may be selected
Test methodology
  Two power levels with interference level constant

## Slide 9: Key test setup for aperiodic CSI test
Channel model
  Static channel model is used
Feedback mode
  TM3 PUSCH 3-0
  TM9 PUSCH 3-1
The following test metrics may be used:
  Reported CQI distribution
  BLER metric
  Delta CQI for the feedback for different power level
  Other test metric are not excluded
Other issues
  Transmission model for each burst is FFS

## Slide 10: Thanks