## Slide 1: 3GPP TSG-RAN WG4 Meeting #78bis San José Del Cabo, México, April 9th –17th, 2016
Ericsson, Intel
Way forward on the signal model for LAA demodulation (Draft)
R4-162754

## Slide 2: Background
In RAN4#78 meeting, the burst transmission model is discussed and several options are listed as:
  Option 1: Explicitly model LBT transmission (Ericsson, R4-160367)
  Option 2: Design a repeated burst transmission pattern. pre-define 8 types of burst pattern, after the previous burst transmission, randomly decide to chose which burst type out of 8 types (Huawei, R4-160742)
  Option 3: Define DL burst transmission model based on Poisson arrival process. Number of subframes in a transmission burst is chosen uniformly from {4,5,6,7,8}. (QC, R4-160046)
  More input from other companies are highly welcome.
In RAN4#78bis meeting, more contributions are submitted for this issue.

## Slide 3: WF on the signal model (Option 1)
Determination of burst format
  Select the number of subframes randomly from {1,3,5,8} with equal probability
  If initial partial subframe is supported by UE, select start symbol for initial subframe randomly from {0, 7} with equal probability. Otherwise, start symbol of initial subframe is always 0.
  If end partial subframe is supported by UE, select number of OFDM symbols in end subframe randomly from {3,6,12,14} with equal probability. Otherwise, end subframe always has 14 OFDM symbols.
  If the said decided burst format is not valid according to RAN1 specification, the number of subframes will be re-selected until a valid burst format is selected

## Slide 4: WF on the signal model (Option 1)
At the end of each transmitted/muted burst
  TE determines burst format
  TE generates a uniform random variable from [0, 1]
  If random variable is less than p=[0.5]
    If both end subframe of previous burst and initial subframe of new burst is full subframe, start burst transmission after deferring one subframe
  Otherwise, start transmission from the latest start symbol determined from the determined burst format
  Otherwise, mute burst transmission
    Muting duration is same as number of subframe for determined burst format

## Slide 5: Background of Pattern based TX model (option 2)
Analysis LAA UE performances under equal conditions.
  LAA UEs are tested and evaluated under identical burst conditions and TB sizes configurations.
  Reduce performance/observation variation due to TX variation in UE performance study.
  Serving cell TB size is fixed based on patterns.
  TX Patterns are made with the worst case assumption (i.e. short burst TB size, short burst time gap )
  Easiness of TE implementation and test maintenance.

## Slide 6: WF on the signal model (Option 2)
Transmitting burst periodically with a fixed periodicity and the fixed test duration
Time interval between pattern transmissions
  Interval is selected randomly.
    Interval should be limited to the range of, X is the transmission periodicity.
Fixed burst transmission length
  Fixed total transmitting TB sizes within on Burst

## Slide 7: WF on the signal model (Option 2)
Sweep the burst patterns in order or randomly select pattern for each periodicity
Initial partial subframes and ending partial subframes are swept with pattern optionally.
  Initial partial subframe / intial full subframe are configured by toggling per a pattern cycle.
  Ending partial subframe [ 3, 6, 9, 10, 11, 12, 14 ] is swept per a pattern cycle.
  See R4-161659 page 5.

## Slide 8: For Information on Option 2 (1)
For absolute performance comparison across companies results :
  Set a burst pattern with a cycle.
  Fix a TB size per a burst pattern.
  Patterns and cycle definition are TBD.
  Example is provided in the next page

## Slide 9: For Information on Option 2 (2)
Example
A Bit indicates
BurstTransmissionLLAbitmap1 = [ 1 1 0 0 1 1 1 1 0 0; 1 1 1 0 0 0 0 0 1 1; 1 1 0 0 1 1 0 0 0 0; 0 0 0 0 0 0 0 0 0 0;]
BurstTransmissionLLAbitmap2 = [ 1 0 0 1 1 1 0 0 1 1; 0 1 0 0 1 1 1 0 0 1; 1 1 0 0 0 0 1 1 0 0; 0 0 0 0 0 0 0 0 0 0;]
BurstTransmissionLLAbitmap3 = [ 1 1 1 1 1 1 1 1 0 0; 0 0 0 0 0 0 0 0 0 0; 0 1 1 1 1 1 1 1 0 0; 0 0 0 0 0 0 0 0 0 0;]
BurstTransmissionLLAbitmap4 = [ 1 0 0 1 0 0 1 0 0 0; 1 0 0 0 1 1 1 0 0 0; 1 1 1 1 1 1 1 1 0 0; 0 0 0 0 0 0 0 0 0 0;]
Total number of SF in a burst = 15 SFs.
Random variable 1 : Tdelta : Pattern Delay randomly selected of [0 : 1ms :10ms]
Random variable 2 : iset : Pattern selection from the burst set [1:1:4]
Defer time can be applied to a burst transmission optionally.