## Slide 1: Way forward on 4Rx CQI
Ericsson
3GPP TSG-RAN WG4 Meeting #78bis R4-162769
San Jose del Cabo, Mexico, 11-15 April, 2016

## Slide 2: Background
Following CQI tests are agreed:
  AWGN
    Test 1: CRS Rank 1: TM1 based on 9.2.1.1 & 9.2.1.2
    Test 2: CSI-RS Rank 2: TM9 based on 9.2.3.1 & 9.2.3.2
    Test 3: CRS Rank 4: TM4 based on 9.2.2.1 & 9.2.2.2
    Test 4: CSI-RS Rank 3: TM9 based on 9.2.3.1 & 9.2.3.2
  Fading
    Test 5: CRS Rank 1: TM1. Based on 9.3.5.1
    Test 6: CSI-RS Rank 1. TM9, Based on 9.3.5.2
WF with detailed test configurations and test point proposals based on alignment results in this week

## Slide 3: Assumptions CRS Rank 1 (FDD and TDD)
Parameter |  | Unit | Test 1 |  | Test 2 | 
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 1 |  |  | 
Downlink power allocation |  | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
Propagation condition and antenna configuration |  |  | AWGN (1 x 4) |  |  | 
SNR (Note 2) |  | dB | SNR1 | SNR2 | SNR3 | SNR4
Ioc |  | dB[mW/15kHz] | Noc+SNR1 | Noc+SNR2 | Noc+SNR3 | Noc+SNR4
Noc |  | dB[mW/15kHz] | -98 |  | -98 | 
Max number of HARQ transmissions |  |  | 1 |  |  | 
Physical channel for CQI reporting |  |  | PUCCH Format 2 (FDD) or PUSCH (TDD) |  |  | 
PUCCH Report Type |  |  | 4 |  |  | 
Reporting periodicity |  | ms | Npd = 5 |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 6 (FDD) or 3 (TDD) |  |  | 
ACK/NACK feedback mode (TDD) |  |  | Multiplexing (TDD) |  |  | 

## Slide 4: Assumptions CSI-RS Rank 2 (FDD)
Parameter |  | Unit | Test 1 |  | Test 2 | 
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 9 |  |  | 
Downlink power allocation |  | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
 |  | dB | -3 |  |  | 
 |  | dB | -3 |  |  | 
Cell-specific reference signals |  |  | Antenna ports 0, 1 |  |  | 
CSI reference signals |  |  | Antenna ports 15,…,18 |  |  | 
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  |  | 5/1 |  |  | 
CSI reference signal configuration |  |  | 0 |  |  | 
Propagation condition and antenna configuration |  |  | Clause B.1 (4 x 4) |  |  | 
Beamforming Model |  |  | As specified in Section B.4.3 |  |  | 
CodeBookSubsetRestriction bitmap |  |  | 0x0000 0000 0100 0000 |  |  | 
SNR (Note 2) |  | dB | SNR1 | SNR2 | SNR3 | SNR4
 |  | dB[mW/15kHz] | Noc+SNR1 | Noc+SNR2 | Noc+SNR3 | Noc+SNR4
 |  | dB[mW/15kHz] | -98 |  | -98 | 
Max number of HARQ transmissions |  |  | 1 |  |  | 
Physical channel for CQI/PMI reporting |  |  | PUSCH (Note3) |  |  | 
PUCCH Report Type for CQI/PMI |  |  | 2 |  |  | 
Physical channel for RI reporting |  |  | PUCCH Format 2 |  |  | 
PUCCH Report Type for RI |  |  | 3 |  |  | 
Reporting periodicity |  | ms | Npd = 5 |  |  | 
CQI delay |  | ms | 8 |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 2 |  |  | 
ri-ConfigIndex |  |  | 1 |  |  | 

## Slide 5: Assumptions CSI-RS Rank 2 (TDD)
Parameter |  | Unit | Test 1 |  | Test 2 | 
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 9 |  |  | 
Uplink downlink configuration |  |  | 2 |  |  | 
Special subframe configuration |  |  | 4 |  |  | 
Downlink power allocation |  | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
 |  | dB | -6 |  |  | 
 |  | dB | -3 |  |  | 
Cell-specific reference signals |  |  | Antenna ports 0, 1 |  |  | 
CSI reference signals |  |  | Antenna ports 15,…,18 |  |  | 
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  |  | 5/3 |  |  | 
CSI reference signal configuration |  |  | 0 |  |  | 
Propagation condition and antenna configuration |  |  | Clause B.1 (4 x 4) |  |  | 
Beamforming Model |  |  | As specified in Section B.4.3 |  |  | 
CodeBookSubsetRestriction bitmap |  |  | 0x0000 0000 0020 0000 0000 0001 0000 |  |  | 
SNR (Note 2) |  | dB | SNR1 | SNR2 | SNR3 | SNR4
 |  | dB[mW/15kHz] | Noc+SNR1 | Noc+SNR2 | Noc+SNR3 | Noc+SNR4
 |  | dB[mW/15kHz] | -98 |  | -98 | 
Max number of HARQ transmissions |  |  | 1 |  |  | 
Physical channel for CQI/PMI reporting |  |  | PUSCH (Note3) |  |  | 
PUCCH Report Type for CQI/PMI |  |  | 2 |  |  | 
Physical channel for RI reporting |  |  | PUSCH |  |  | 
PUCCH Report Type for RI |  |  | 5 |  |  | 
Reporting periodicity |  | ms | Npd = 5 |  |  | 
CQI delay |  | ms | 10 or 11 |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 3 |  |  | 
ri-ConfigIndex |  |  | 805 |  |  | 
ACK/NACK feedback mode |  |  | Multiplexing |  |  | 

## Slide 6: Assumptions CRS Rank 4 (FDD)
Parameter |  | Unit | Test 1 |  | Test 2 | 
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 4 |  |  | 
Downlink power allocation |  | dB | -3 |  |  | 
 |  | dB | -3 |  |  | 
 |  | dB | 0 |  |  | 
Propagation condition and antenna configuration |  |  | Clause B.1 (4 x 4) |  |  | 
CodeBookSubsetRestriction bitmap |  |  | 0x0002 0000 0000 0000 |  |  | 
SNR (Note 2) |  | dB | SNR1 | SNR2 | SNR3 | SNR4
 |  | dB[mW/15kHz] | Noc+SNR1 | Noc+SNR2 | Noc+SNR3 | Noc+SNR4
 |  | dB[mW/15kHz] | -98 |  | -98 | 
Max number of HARQ transmissions |  |  | 1 |  |  | 
Physical channel for CQI/PMI reporting |  |  | PUCCH Format 2 |  |  | 
PUCCH Report Type for CQI/PMI |  |  | 2 |  |  | 
PUCCH Report Type for RI |  |  | 3 |  |  | 
Reporting periodicity |  | ms | Npd = 5 |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 6 |  |  | 
ri-ConfigIndex |  |  | 1 (Note 3) |  |  | 

## Slide 7: Assumptions CRS Rank 4 (TDD)
Parameter |  | Unit | Test 1 |  | Test 2 | 
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 4 |  |  | 
Uplink downlink configuration |  |  | 2 |  |  | 
Special subframe configuration |  |  | 4 |  |  | 
Downlink power allocation |  | dB | -3 |  |  | 
 |  | dB | -3 |  |  | 
 |  | dB | 0 |  |  | 
Propagation condition and antenna configuration |  |  | Clause B.1 (4 x 4) |  |  | 
CodeBookSubsetRestriction bitmap |  |  | 0x0002 0000 0000 0000 |  |  | 
SNR (Note 2) |  | dB | SNR1 | SNR2 | SNR3 | SNR4
 |  | dB[mW/15kHz] | Noc+SNR1 | Noc+SNR2 | Noc+SNR3 | Noc+SNR4
 |  | dB[mW/15kHz] | -98 |  | -98 | 
Max number of HARQ transmissions |  |  | 1 |  |  | 
Physical channel for CQI/PMI reporting |  |  | PUSCH (Note 3) |  |  | 
PUCCH Report Type |  |  | 2 |  |  | 
Reporting periodicity |  | ms | Npd = 5 |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 3 |  |  | 
ri-ConfigIndex |  |  | 805 (Note 4) |  |  | 
ACK/NACK feedback mode |  |  | Multiplexing |  |  | 

## Slide 8: Assumptions CSI-RS Rank 3 (FDD)
Parameter |  | Unit | Test 1 |  | Test 2 | 
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 9 |  |  | 
Downlink power allocation |  | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
 |  | dB | -3 |  |  | 
 |  | dB | -3 |  |  | 
Cell-specific reference signals |  |  | Antenna ports 0, 1 |  |  | 
CSI reference signals |  |  | Antenna ports 15,…,18 |  |  | 
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  |  | 5/1 |  |  | 
CSI reference signal configuration |  |  | 0 |  |  | 
Propagation condition and antenna configuration |  |  | Clause B.1 (4 x 4) |  |  | 
Beamforming Model |  |  | As specified in Section B.4.3 |  |  | 
CodeBookSubsetRestriction bitmap |  |  | 0x0000 0020 0000 0000 |  |  | 
SNR (Note 2) |  | dB | SNR1 | SNR2 | SNR3 | SNR4
 |  | dB[mW/15kHz] | Noc+SNR1 | Noc+SNR2 | Noc+SNR3 | Noc+SNR4
 |  | dB[mW/15kHz] | -98 |  | -98 | 
Max number of HARQ transmissions |  |  | 1 |  |  | 
Physical channel for CQI/PMI reporting |  |  | PUSCH (Note3) |  |  | 
PUCCH Report Type for CQI/PMI |  |  | 2 |  |  | 
Physical channel for RI reporting |  |  | PUCCH Format 2 |  |  | 
PUCCH Report Type for RI |  |  | 3 |  |  | 
Reporting periodicity |  | ms | Npd = 5 |  |  | 
CQI delay |  | ms | 8 |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 2 |  |  | 
ri-ConfigIndex |  |  | 1 |  |  | 

## Slide 9: Assumptions CSI-RS Rank 3 (TDD)
Parameter |  | Unit | Test 1 |  | Test 2 | 
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 9 |  |  | 
Uplink downlink configuration |  |  | 2 |  |  | 
Special subframe configuration |  |  | 4 |  |  | 
Downlink power allocation |  | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
 |  | dB | -6 |  |  | 
 |  | dB | -3 |  |  | 
CRS reference signals |  |  | Antenna ports 0, 1 |  |  | 
CSI reference signals |  |  | Antenna ports 15,…,22 |  |  | 
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  |  | 5/ 3 |  |  | 
CSI reference signal configuration |  |  | 0 |  |  | 
Propagation condition and antenna configuration |  |  | Clause B.1 (8 x 4) |  |  | 
Beamforming Model |  |  | As specified in Section B.4.3 |  |  | 
CodeBookSubsetRestriction bitmap |  |  | 0x0000 0020 0000 0000 |  |  | 
SNR (Note 2) |  | dB | SNR1 | SNR2 | SNR3 | SNR4
 |  | dB[mW/15kHz] | Noc+SNR1 | Noc+SNR2 | Noc+SNR3 | Noc+SNR4
 |  | dB[mW/15kHz] | -98 |  | -98 | 
Max number of HARQ transmissions |  |  | 1 |  |  | 
Physical channel for CQI/PMI reporting |  |  | PUSCH (Note 3) |  |  | 
PUCCH Report Type for CQI/second PMI |  |  | 2b |  |  | 
Physical channel for RI reporting |  |  | PUSCH |  |  | 
PUCCH Report Type for RI/ first PMI |  |  | 5 |  |  | 
Reporting periodicity |  | ms | Npd = 5 |  |  | 
CQI delay |  | ms | 10 or 11 |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 3 |  |  | 
ri-ConfigIndex |  |  | 805 (Note 4) |  |  | 
ACK/NACK feedback mode |  |  | Multiplexing |  |  | 

## Slide 10: Assumptions fading CRS (FDD) 9.3.5.1.1
Parameter | Unit | Cell 1 | Cell 2
Bandwidth | MHz | 10 MHz | 
Transmission mode |  | 1 (port 0) | 
Cyclic Prefix |  | Normal | Normal
Cell ID |  | 0 | 1
SINR (Note 8) | dB | TBD | N/A
 | dB[mW/15kHz] | -98 | N/A
Propagation channel |  | EPA5 | Static (Note 7)
Correlation and antenna configuration |  | Low (1 x 4) | (1 x 4)
DIP (Note 4) | dB | N/A | -0.41
Reference measurement channel |  | Note 2 | R.2 FDD
Reporting mode |  | PUCCH 1-0 | N/A
Reporting periodicity | ms | Npd = 2 | N/A
CQI delay | ms | 8 | N/A
Physical channel for CQI reporting |  | PUSCH (Note 3) | N/A
PUCCH Report Type |  | 4 | N/A
cqi-pmi-ConfigurationIndex |  | 1 | N/A
Max number of HARQ transmissions |  | 1 | N/A

## Slide 11: Assumptions fading CRS (TDD) 9.3.5.1.2
Parameter | Unit | Cell 1 | Cell 2
Bandwidth | MHz | 10 MHz | 
Transmission mode |  | 1 (port 0) | 
Uplink downlink configuration |  | 2 | 
Special subframe configuration |  | 4 | 
Cyclic Prefix |  | Normal | Normal
Cell ID |  | 0 | 1
SINR (Note 8) | dB | TBD | N/A
 | dB[mW/15kHz] | -98 | -98
Propagation channel |  | EPA5 | Static (Note 7)
Correlation and antenna configuration |  | Low (1 x 4) | (1 x 4)
DIP (Note 4) | dB | N/A | -0.41
Reference measurement channel |  | Note 2 | R.2A TDD
Reporting mode |  | PUCCH 1-0 | N/A
Reporting periodicity | ms | Npd = 5 | N/A
CQI delay | ms | 10 or 11 | N/A
Physical channel for CQI reporting |  | PUSCH (Note 3) | N/A
PUCCH Report Type |  | 4 | N/A
cqi-pmi-ConfigurationIndex |  | 3 | N/A
Max number of HARQ transmissions |  | 1 | N/A
ACK/NACK feedback mode |  | Multiplexing | N/A

## Slide 12: Assumptions fading CSI-RS (FDD) 9.3.5.2.1
Parameter | Unit | Cell 1 | Cell 2
Bandwidth | MHz | 10 MHz | 
Transmission mode |  | 9 | 
Cyclic Prefix |  | Normal | Normal
Cell ID |  | 0 | 1
SINR (Note 8) | dB | TBD | N/A
 | dB[mW/15kHz] | -98 | N/A
Propagation channel |  | EPA5 | Static (Note 7)
Correlation and antenna configuration |  | Low (2 x 4) | (1 x 4)
DIP (Note 4) | dB | N/A | -0.41
Cell-specific reference signals |  | Antenna ports 0,1 | Antenna port 0
CSI reference signals |  | Antenna ports 15-18 | N/A
CSI-RS periodicity and subframe offset |  | 5/1 | N/A
CSI-RS reference signal configuration |  | 2 | N/A
Zero-power CSI-RS configuration ICSI-RS / ZeroPowerCSI-RS bitmap | Subframes / bitmap | N/A | 1 / 0010000000000000
CodeBookSubsetRestriction bitmap |  | 001111 | N/A
Reference measurement channel |  | Note 2 | R.2 FDD
Reporting mode |  | PUCCH 1-1 | N/A
Reporting periodicity | ms | Npd = 5 | N/A
CQI delay | ms | 8 | N/A
Physical channel for CQI/PMI reporting |  | PUSCH (Note 3) | N/A
PUCCH Report Type for CQI/PMI |  | 2 | N/A
PUCCH channel for RI reporting |  | PUCCH Format 2 | N/A
PUCCH Report Type for RI |  | 3 | N/A
cqi-pmi-ConfigurationIndex |  | 2 | N/A
ri-ConfigIndex |  | 1 | N/A
Max number of HARQ transmissions |  | 1 | N/A

## Slide 13: Assumptions fading CSI-RS (TDD) 9.3.5.2.2
Parameter | Unit | Cell 1 | Cell 2
Bandwidth | MHz | 10 MHz | 
Transmission mode |  | 9 | 
Uplink downlink configuration |  | 2 | 
Special subframe configuration |  | 4 | 
Cyclic Prefix |  | Normal | Normal
Cell ID |  | 0 | 1
SINR (Note 8) | dB | T BD | N/A
 | dB[mW/15kHz] | -98 | -98
Propagation channel |  | EPA5 | Static (Note 7)
Correlation and antenna configuration |  | Low (2 x 4) | (1 x 4)
DIP (Note 4) | dB | N/A | -0.41
Cell-specific reference signals |  | Antenna ports 0,1 | Antenna port 0
CSI reference signals |  | Antenna ports 15-18 | N/A
CSI-RS periodicity and subframe offset |  | 5/3 | N/A
CSI-RS reference signal configuration |  | 2 | N/A
Zero-power CSI-RS configuration ICSI-RS / ZeroPowerCSI-RS bitmap | Subframes / bitmap | N/A | 3 / 0010000000000000
CodeBookSubsetRestriction bitmap |  | 001111 | N/A
Reference measurement channel |  | Note 2 | R.2A TDD
Reporting mode |  | PUCCH 1-1 | N/A
Reporting periodicity | ms | Npd = 5 | N/A
CQI delay | ms | 10 | N/A
Physical channel for CQI/PMI reporting |  | PUSCH (Note 3) | N/A
PUCCH Report Type for CQI/PMI |  | 2 | N/A
Physical channel for RI reporting |  | PUCCH Format 2 | N/A
PUCCH Report Type for RI |  | 3 | N/A
cqi-pmi-ConfigurationIndex |  | 3 | N/A
ri-ConfigIndex |  | 805 (Note 9) | N/A
Max number of HARQ transmissions |  | 1 | N/A
ACK/NACK feedback mode |  | Multiplexing | N/A

## Slide 14: Way forward
Evaluate requirements on following slides
TBDs to be agreed on by email

## Slide 15: Way Forward on 4Rx CQI reporting AWGN
CRS Rank 1 (FDD)
  For the Low group Evaluate at least the following SNRs
    SNR1={-3, -2, -1, 0}
    SNR2=SNR1+1
  For the High group Evaluate at least the following SNRs
    SNR3={3, 4, 5, 6}
    SNR4=SNR3+1

## Slide 16: Way Forward on 4Rx CQI reporting AWGN
CRS Rank 1 (TDD)
  For the Low group Evaluate at least the following SNRs
    SNR1={TBD}
    SNR2=SNR1+1
  For the High group Evaluate at least the following SNRs
    SNR3={TBD}
    SNR4=SNR3+1

## Slide 17: Way Forward on 4Rx CQI reporting AWGN
CSI-RS Rank 2 (FDD)
  For the Low group Evaluate at least the following SNRs
    SNR1={2,3,4,5}
    SNR2=SNR1+1
  For the High group Evaluate at least the following SNRs
    SNR3={8,9,10,11}
    SNR4=SNR3+1

## Slide 18: Way Forward on 4Rx CQI reporting AWGN
CSI-RS Rank 2 (TDD)
  For the Low group Evaluate at least the following SNRs
    SNR1={TBD}
    SNR2=SNR1+1
  For the High group Evaluate at least the following SNRs
    SNR3={TBD}
    SNR4=SNR3+1

## Slide 19: Way Forward on 4Rx CQI reporting AWGN
CRS Rank 4 (FDD)
  For the Low group Evaluate at least the following SNRs
    SNR1={5,6}
    SNR2=SNR1+1
  For the High group Evaluate at least the following SNRs
    SNR3={11,12}
    SNR4=SNR3+1

## Slide 20: Way Forward on 4Rx CQI reporting AWGN
CRS Rank 4 (TDD)
  For the Low group Evaluate at least the following SNRs
    SNR1={TBD}
    SNR2=SNR1+1
  For the High group Evaluate at least the following SNRs
    SNR3={TBD}
    SNR4=SNR3+1

## Slide 21: Way Forward on 4Rx CQI reporting AWGN
CSI-RS Rank 3 (FDD)
  For the Low group Evaluate at least the following SNRs
    SNR1={4,5}
    SNR2=SNR1+1
  For the High group Evaluate at least the following SNRs
    SNR3={10,11}
    SNR4=SNR3+1

## Slide 22: Way Forward on 4Rx CQI reporting AWGN
CSI-RS Rank 3 (TDD)
  For the Low group Evaluate at least the following SNRs
    SNR1={4,5}
    SNR2=SNR1+1
  For the High group Evaluate at least the following SNRs
    SNR3={10,11}
    SNR4=SNR3+1

## Slide 23: Way forward Fading requirements 9.3.5
Evaluate and present at RAN4#79:
  Throughputs with and without neighbor cell interference,
  gamma and
  BLER with neighbour cell interference
for every studied SNR