## Slide 1: Way forward on 4Rx PMI with 1 Layer
Ericsson
3GPP TSG-RAN WG4 Meeting #78bis R4-162770
San Jose del Cabo, Mexico, 11-15 April, 2016

## Slide 2: Background Rank 1
Agreements
  Agree to have rank 1 TDD 8x4 PMI tests

## Slide 3: Assumptions PMI Rank 1 CRS (TDD)
Parameter |  | Unit | Test 1
Bandwidth |  | MHz | 10
Transmission mode |  |  | 9
Uplink downlink configuration |  |  | 1
Special subframe configuration |  |  | 4
Propagation channel |  |  | EVA5
Precoding granularity |  | PRB | 50
Antenna configuration |  |  | 8 x 4
Correlation modeling |  |  | High, Cross polarized
Cell-specific reference signals |  |  | Antenna ports 0,1
CSI reference signals |  |  | Antenna ports 15,…,22
Beamforming model |  |  | Annex B.4.3
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  |  | 5/ 4
CSI-RS reference signal configuration |  |  | 0
CodeBookSubsetRestriction bitmap |  |  | 0x0000 0000 001F FFE0 0000 0000 FFFF
Downlink power allocation |  | dB | 0
 |  | dB | 0
 | Pc | dB | -6
 |  | dB | -3
 |  | dB[mW/15kHz] | -98
Reporting mode |  |  | PUSCH 3-1
Reporting interval |  | ms | 5
PMI delay (Note 2) |  | ms | 10
Measurement channel |  |  | R.45 TDD (MCS 12) and MCS 19
OCNG Pattern |  |  | OP.1 TDD
Max number of HARQ transmissions |  |  | 4
Redundancy version coding sequence |  |  | {0,1,2,3}/{0,0,1,2}
ACK/NACK feedback mode |  |  | Multiplexing
Based on 9.4.1.3.2

## Slide 4: Way Forward
Evaluate rank 1 test for fixed reference channel MCS 12 and MCS 19 based on the simulation assumptions
Contribute with the throughputs at random PMI and follow PMI and ratio of throughputs g for the SNR
Contribute with g, for the SNR when the throughput of the follow PMI simulation is 70% of the max throughput, as the alignment value.