## Slide 1: Way forward on 4Rx PMI with multiple layers
Ericsson
3GPP TSG-RAN WG4 Meeting #78bis R4-162771
San Jose del Cabo, Mexico, 11-15 April, 2016

## Slide 2: Background 3-4 Layers
No agreements in the adhoc

## Slide 3: Evaluation for PMI test for 3 Layers
Parameter |  | Unit | Test 1
Bandwidth |  | MHz | 10
Transmission mode |  |  | 9
Uplink downlink configuration |  |  | 1
Special subframe configuration |  |  | 4
Propagation channel |  |  | EVA5
Precoding granularity |  | PRB | 50
Antenna configuration |  |  | 8 x 4
Cell-specific reference signals |  |  | Antenna ports 0,1
CSI reference signals |  |  | Antenna ports 15,…,22
Beamforming model |  |  | Annex B.4.3
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  |  | 5/ 4
CSI-RS reference signal configuration |  |  | 0
CodeBookSubsetRestriction bitmap |  |  | TBD
Downlink power allocation |  | dB | 0
 |  | dB | 0
 | Pc | dB | -6
 |  | dB | -3
 |  | dB[mW/15kHz] | -98
Reporting mode |  |  | PUSCH 3-1
Reporting interval |  | ms | 5
PMI delay (Note 2) |  | ms | 10
OCNG Pattern |  |  | OP.1 TDD
Max number of HARQ transmissions |  |  | 4
Redundancy version coding sequence |  |  | {0,1,2,3}
ACK/NACK feedback mode |  |  | Multiplexing
Variable Parameters | 
SNR range | TBD
Antenna Correlation | Medium Correlation A with crosspolarized antennas 8x4
 | Medium Correlation A with ULA 8x4
Measurement Channel | Follow CQI for follow PMI and random PMI
 | Follow CQI for follow PMI and Fixed MCS for random PMI

## Slide 4: Way Forward 3 Layers
Study PMI 3 Layers
Based on the options on previous slide evaluate the test and propose 3 Layer PMI test
The TBDs to be agreed by email