## Slide 1: WF on simulation assumption of downlink CCH-IM receiver in asynchronous networks for PDCCH/PCFICH/PHICH
Huawei, [xx]
3GPP TSG-RAN WG4 Meeting # 78bis San Jose del Cabo, Mexico, 11 – 15 Apr 2016
Agenda Item: 6.3
R4-162798

## Slide 2: Background
In RAN #71 meeting (RP-160594, March, 2016), it was agreed to evaluate reference IM receiver for PDCCH/PCFICH/PHICH in asynchronous networks:
  Evaluate reference IM receiver structure for PDCCH/PCFICH/PHICH in asynchronous network
    The async network related requirements/test cases may or may not be introduced in this WI. This shall be decided based on the conclusion of the evaluation by RAN4#79. The WI should be completed within Rel-13.
This WF provides candidate reference receiver(s) and simulation assumptions for evaluation purpose.

## Slide 3: Way Forward
Candidate reference IM receiver for PDCCH/PCFICH/PHICH in asynchronous networks
  Reference IM receiver: LMMSE-IRC
  Legacy receiver: LMMSE-MRC
Companies are encourage to bring results based on above two receivers and following assumptions.

## Slide 4: Simulation Assumptions
  Interference modelling
  *the interference signal arrive later after serving signal, taking 1/7 subframe time-offset for example:
Parameters | Case 1 | Case 2
PDSCH interference | Rel-11 Type A receiver asynchronous interference model (TS 36.101 B.5.3, 8.2.1.4.1B) | TM4 rank-1, 100% PDSCH loading, different/random PMI for each subframe
Time offset* | 1/3 and 2/3 subframes | 1/7 and 1/14 subframes
Cell ID | (0, 1, 2) | (0,1,2)
Interference power profile | DIP1:-1.73; DIP2: -8.66 | Low INR: I1/Noc = 3.28 dB, I2/Noc = 0.74 dB Medium INR: I1/Noc = 7.77 dB, I2/Noc = 2.29 dB
PDCCH interference | 100% PDCCH/PCFICH/PHICH loading | 
Frequency offset | 0 Hz between all cells | 

## Slide 5: Simulation Assumptions
Common parameters | 
System bandwidth | 10MHz for both serving cell and interfering cells
Duplexing mode | FDD
Cyclic prefix | Normal
Number of interference cells | 2 interfering cells
CRS ports | Port 0 and 1
Antenna configuration | 2x2 with Low correlation
Tx EVM | 6%
Unused Serving cell RE-s and PRB-s | OCNG
Channel model | EVA70
Number of PHICH groups (Ng) | 1
PHICH duration | Normal
PDCCH/PCFICH parameters | 
Serving cell PDCCH | AL 2, 4; DCI Format 2 (43 bits – FDD, 10MHz)
CFI | CFIS = 3, CFII = 3
Performance metrics | Pm-dsg vs SINR
PHICH parameters | 
PHICH FRC | R.19 in TS 36.101
CFI | CFIS = 1, CFII = 1
Performance metrics | Pm-an vs SINR
  Other parameters