## Slide 1: Way forward on UE EVM measurement for NB-IoT
Huawei, Hisilicon, Neul, Qualcomm, …
3GPP TSG-RAN WG4 Meeting #78bis R4-162824 San Jose del Cabo, Mexico, 11 – 15 April, 2016

## Slide 2: Background
It is discussed in [1],
  The number of CP samples that are distorted by the transmit filtering/windowing increases when NB-IoT bandwidth reduces, these distorted samples should be excluded from the EVM measurement, which is reflected in the ratio of the EVM window duration to the CP duration.
  In the case of an NB-IoT transmission using less than 12 subcarriers, the EVM measurement accuracy would be degraded due to the reduced number of symbols that are considered.
[1] R4-162316, “NB-IoT EVM measurement method for uplink”, Huawei, Hisilicon, Neul

## Slide 3: Proposals
EVM measurements for NB-PUSCH both using 3.75kHz and 15 kHz subcarrier spacing, the method in Annex F.4 of TS 36.101 is re-used.
EVM measurement window length (at 1.92MHz sampling rate) for NB-PUSCH is defined not larger than 5.
  Detail value of window length is FFS.
Others related to EVM measurement need further investigation,
  EVM measurement window length for NB-PRACH.
  EVM measurement duration for NB-PUSCH.
  EVM measurement duration for NB-PRACH.