## Slide 1: Way forward on NB-IoT RRM measurement
Huawei, HiSilicon, Qualcomm, Ericsson, Nokia
R4-162835
3GPP TSG-RAN WG4 #78bis
San Jose Del Cabo, Mexico, 11 – 15 April, 2016
Agenda Item: 6.13.5

## Slide 2: Background
Although the measurement report is not supported for Rel-13 NB-IoT UE, RRM measurement is still an essential UE behavior, e.g. for cell selection/reselection, etc.
In R4-161294, it was agreed that:
  RAN4 is to study RRM measurement performance using following options:
    Option 1: Measurement based on NB-RS signals
      To be used as simulation baseline only.
    Option 2: Measurement based on synchronization signals (e.g. NB-SSS)
      provided that NB-SSS are available for measurement
    Option 3: Measurement based on combination of NB-RS and NB-SSS.
      provided that NB-SSS are available for measurement
    Other options are not precluded

## Slide 3: Consensus on RRM measurement
RSRP for NB-IoT shall be referred to as NRSRP (NarrowBand-RSRP)
RSRQ for NB-IoT shall be referred to as NRSRQ (NarrowBand-RSRQ)
NRSRP is defined as:
  the linear average over the power contributions (in [W]) of the resource elements that carry cell-specific reference signals within the considered measurement frequency bandwidth.
  For RSRP determination the cell-specific reference signals R0 according to TS 36.211 [3] shall be used.
  It is FFS if R1 may be used in addition to R0 to determine RSRP.
  The reference point for the RSRP shall be the antenna connector of the UE.
NRSRQ is defined as “to be defined”

## Slide 4: Consensus on RRM measurement
RAN4 is to define NRSRP/NRSRQ measurement requirements based on NB-RS measurement for Rel-13 NB-IoT
  Applicable requirements for RRC_IDLE and RRC_CONNECTED modes are to be defined
  UE is allowed to perform measurement using either NB-RS or NB-SSS or a combination of these signals for RRM measurement
RAN4 is discuss whether to specify different NRSRP/NRSRQ measurement accuracy and measurement period for each coverage mode
RAN4 agreed that the minimum number of inter-frequency carriers that the NB-IoT UE shall be able to monitor is [2] (excluding serving carrier)
  It is FFS whether to specify minimum number of inter-frequency carriers to monitor per deployment mode(in-band/standalone/guard-band)
RAN4 is to define inter-frequency measurement requirements treating all carriers as normal performance carriers as in Rel-11
  IncMon framework will not be used since number carriers is expected to be small

## Slide 5: Simulation assumptions for RRM measurement
Note: RSSI is measured only from OFDM symbols containing NB-RS of measurement subframes.
Parameters | Value | Comments
Measurement bandwidth | 1 resource blocks | Both RSRP and RSRQ measured over 1 RB
System bandwidth | 1 resource blocks | 
L1 measurement period | 200 ms, 400 ms, 800 ms 1600 ms | Even further increased measurement period can be considered to evaluate the measurement performance
Sample duration | 1ms, 3ms, 6ms, 10ms | Even further increased sampling period can be considered to evaluate the measurement performance
Measurement sampling rate | Once every 40ms or 80 ms | Sample period: 40ms or 80ms
L3 filtering | Disabled | 
DRX | OFF | 
Antenna configuration | 1TX, 1RX | 
Mobility | Stationary UEs, | 
Channel model | AWGN, ETU 1Hz, EPA 1Hz | Models stationary device
Measurement type | NB-RS only based | Companies are encouraged to provide simulation results for measurements based on follows signals. NB-RS is to be used as baseline for simulation only.
CP length | Normal | 
Carrier frequency | 2 GHz | 
Ec/Iot | -20 dB, …, 10 dB | AWGN noise
Frequency error modelling | +/-50 Hz | With respect to reference cell