## Slide 1: WF on REFSENS for NB-IoT
Sony, Intel,……
R4-162864
3GPP TSG RAN WG1 #84 bis
San Jose del Cabo, Mexico, 11 - 15 April, 2016
Agenda item 6.23.3

## Slide 2: Background
REFSENS calculation
PREFSENS (dBm)= -174dBm + 10log10B + NF + IM + RIL +[ N1/f ] + SNR
    -174dBm noise floor at room temperature in B=1Hz (1.38*10-23*300)
    B operating bandwidth in Hz
    NF Noise figure in dB of the receiver in antenna connector
    IM Implementation and production margin
    RIL Additional band dependent filter loss
    N1/f Noise contribution from DC subcarrier
    SNR Required Signal to Noise Ratio in baseband

## Slide 3: Background
Option 1 Re-use the existing (legacy) REFSENS table and apply the same relaxation for single RX as was agreed for cat 0. Then there would be a scaling from the 5MHz value of 10log10(1RB/25RB) = -14dB. The assumption in this case is that the same SNR for NB IOT as for legacy LTE applies. There is also a band-dependant factor in legacy LTE whose relevance needs to be discussed since only half duplex is considered.
Option 2 The alternative method would be to start all over: determine required SNR (e.g. by simulation), estimate the noise figure for the receiver, and agree on an adequate implementation and production margin. The noise figure of the receiver need to be calculated in antenna connector and may have some frequency dependence (e.g. above/below 1GHz or something). Probably there has to be an agreement on possible reference architectures (SAW filter, SAW-less or maybe both) in order to do the NF calculation.

## Slide 4: Agreement
Option 2 shall be used in deriving REFSENS for NB IOT

## Slide 5: Way Forward
Agree on the following parameters:
  NF for the NB IOT receiver [7 – 9 dB] including
    extreme temperature
  [N1/f term TBD, dB]
  IM for the NB-IOT receiver [2.5] dB
  Band dependent additional filter loss for difficult bands R∆IL [0 – 1.5dB]
    The default value of this factor is 0. Application of non-zero factor for some bands is FFS
Repetitions will be addressed in the specs. Decision how to implement the specs will be addressed during the NB-IoT adhoc meeting according following options:
  Including repetition in the REFSENS spec
  Defining a new REFSENS with repetitions in addition to REFSENS with no repetitions
  Including repetition in an additional demodulation test and REFSENS is tested only without repetitions
Agree on SNR from simulations according to simulation parameters on next page.
Companies are encourage to contribute on the above including SNR simulations.

## Slide 6: Simulation assumptions for SNR
Parameter | Unit | Standalone Case
Channel bandwidth | kHz | 200
Antenna configuration |  | 1x1
Allocated resource blocks |  | 1
Subcarriers per resource block |  | 12
Allocated subframes per Radio Frame |  | 10
Channel Coding |  | TBCC
Modulation |  | QPSK
Target Coding Rate |  | 1/3
Maximum number of HARQ transmissions |  | 1
Information Bit Payload per Sub-Frame |  | [88]
Transport block CRC | Bits | 24
Number of Code Blocks per Sub-Frame |  | 1
Binary Channel Bits Per Sub-Frame |  | [320]
LTE CRS ports |  | N/A
Number of NB-RS ports |  | 1
Number of NB-PDSCH repetitions |  | 1
Channel estimation |  | Companies are encourage to report on simulation assumptions in their simulation results
Channel |  | AWGN
Frequency error |  | None
Timing error |  | None
Power boosting |  | N/A

## Slide 7: References
R4-162610 NB-IoT UE Rx RF Requirements, MediaTek Inc.
R4-162250 UE REFSENS for NB-IoT, Ericsson
R4-162552 WF on REFSENS for NB IOT, Sony