## Slide 1: Way forward on NB-IoT RRM measurement
Huawei, HiSilicon, Qualcomm, Ericsson, Nokia, ZTE, NTT DOCOMO, CMCC
R4-162868
3GPP TSG-RAN WG4 #78bis
San Jose Del Cabo, Mexico, 11 – 15 April, 2016
Agenda Item: 6.13.5

## Slide 2: Background
Although the measurement report is not supported for Rel-13 NB-IoT UE, RRM measurement is still an essential UE behavior, e.g. for cell selection/reselection, etc.
In R4-161294, it was agreed that:
  RAN4 is to study RRM measurement performance using following options:
    Option 1: Measurement based on NB-RS signals
      To be used as simulation baseline only.
    Option 2: Measurement based on synchronization signals (e.g. NB-SSS)
      provided that NB-SSS are available for measurement
    Option 3: Measurement based on combination of NB-RS and NB-SSS.
      provided that NB-SSS are available for measurement
    Other options are not precluded

## Slide 3: Consensus on RRM measurement
RSRP for NB-IoT shall be referred to as NRSRP (NarrowBand-RSRP)
RSRQ for NB-IoT shall be referred to as NRSRQ (NarrowBand-RSRQ)
RAN4 is to define NRSRP/NRSRQ measurement requirements based on NB-RS measurement for Rel-13 NB-IoT
  Applicable requirements for RRC_IDLE and RRC_CONNECTED modes are to be defined
  UE is allowed to perform measurement using either NB-RS or NB-SSS or a combination of these signals for RRM measurement
RAN4 is to discuss whether to specify different NRSRP/NRSRQ measurement accuracy and measurement period for each coverage mode
RAN4 agreed that the minimum number of inter-frequency carriers that the NB-IoT UE shall be able to monitor is [2] (excluding serving carrier)
  It is FFS whether to specify minimum number of inter-frequency carriers to monitor per deployment mode(in-band/standalone/guard-band)
RAN4 is to define inter-frequency measurement requirements treating all carriers as normal performance carriers as in Rel-11
  IncMon framework will not be used since number carriers is expected to be small

## Slide 4: Simulation assumptions for RRM measurement
Note: RSSI is measured only from OFDM symbols containing NB-RS of measurement subframes.
Parameters | Value | Comments
Measurement bandwidth | 1 resource blocks | Both RSRP and RSRQ measured over 1 RB
System bandwidth | 1 resource blocks | 
L1 measurement period | 200 ms, 400 ms, 800 ms 1600 ms | Even further increased measurement period can be considered to evaluate the measurement performance
Sample duration | 1ms, 3ms, 6ms, 10ms | Even further increased sampling period can be considered to evaluate the measurement performance
Measurement sampling rate | Once every 40ms or 80 ms | Sample period: 40ms or 80ms
L3 filtering | Disabled | 
DRX | OFF | 
Antenna configuration | 1TX, 1RX | 
Mobility | Stationary UEs, | 
Channel model | AWGN, ETU 1Hz, EPA 1Hz | Models stationary device
Measurement type | NB-RS only based | 
CP length | Normal | 
Carrier frequency | 2 GHz | 
Ec/Iot | -20 dB, …, 10 dB | AWGN noise
Frequency error modelling | +/-50 Hz | With respect to reference cell