## Slide 1: WF on CA impact of B41 HPUE
CMCC,Sprint, MediaTeK, China Unicom, Samsung, Skyworks,Qorvo, China Telecom, Softbank
3GPP TSG-RAN WG4 Meeting #78 bis R4-162976 San Jose del Cabo, Mexico, 11–15 April 2016

## Slide 2: Background
Objective of the SI
  The study is limited to evaluating the transmission and reception impact and values for single carrier UL operation for Band 41 E-UTRA UE Power Class 2
  Assess Band 41 power class 2 potential impacts to TDD/FDD carrier aggregation band combinations
Impact of B41 HPUE to CA was discussed in RAN4#78bis [1-3]
Legacy CA RF requirements such as ΔTib, ΔRib and desensitization may not be applicable to HPUE due to the newer RF component such as high power PA and RF filter, dependent on the vendor
[1] R4-162655, Impact of HPUE to CA, Qualcomm Incorporated
[2] R4-161885, HPUE impact to CA, MediaTek Inc.
[3] R4-162274, Impact of B41 HPUE to CA_B3_B41, CMCC

## Slide 3: Way Forward
Current B41 related CA requirements only apply to B41 Power Class 3 UE. B41 Power Class 2 UE can operate in B41 related CA only if the Power Class 2 UE fallback to Power Class 3 can meet the current B41 related CA requirements.
The implementation for supporting B41 Power Class 3 CA requirements by B41 Power Class 2 UE fallback mode is not precluded.
B41 related CA requirements for B41 Power Class 2 UE can be identified by proposing separate CA+HPUE WIs for each combination after completion of B41 Power Class 2 single carrier specification.
Approve Text Proposal on slide 4.

## Slide 4: Way Forward
Text Proposal
<<Start Text>>
5.5 Impact to TDD/FDD carrier aggregation band combinations
Current B41-related CA requirements only apply to B41 Power Class 3 UE operation. B41 Power Class 2 UE can operate in B41 related CA only in Power Class 3 fallback mode, which must meet the current B41-related CA requirements. As long as the current B41-related CA requirements are met, implementations supporting both B41 single carrier Power Class 2 and Power Class 3 CA requirements using Power Class 3 fallback mode are not precluded.
CA Requirements for B41 in Power Class 2 can be identified by separate CA+HPUE WIs for each combination, after completion of B41 Power Class 2 single carrier specification.
<< End Text>>