## Slide 1: WF on eMTC RLM CEMode A test
Nokia, Anritsu, Ericsson, Qualcomm
R4-163025
3GPP TSG-RAN WG4 Meeting #78bis
San Jose del Cabo, Mexico, April 11 – 15, 2016
Agenda Item: 6.5.1

## Slide 2: Proposals
The following test setups are common for non-DRX and DRX tests.
  The combination of aggregation level and repetition (AL,R) used for the hypothetic M-PDCCH transmission is randomly selected in each run during the test from the two sets of parameters below.
    Set 1: OoS (24, 8), IS (8,4)
    Set 2: OoS (16, 4), IS (4,2)
  Margins used to derive the SNR levels from Qin/out are to be decided in RAN4#79.
  Periodic CQI reporting is used to for test verification, with the same configuration as in legacy RLM tests. PUCCH format 2 repetition is not configured.
  Note: The feasibility of periodic CQI reporting values can be re-visited if problem is identified.
  Companies are encouraged to provide simulation results on Qin and Qout values for the two sets of combinations. Simulation assumptions are listed in next slide.

## Slide 3: M-PDCCH simulation assumptions
Parameter | M-PDCCH (CE Mode A)
DCI format | DCI Format 6-1A
System Bandwidth | 10 MHz
Channel model | AWGN ETU 30 Hz
Antenna configuration | 2x1
Number of information bits (incl. 16 bits CRC) | FDD and HD-FDD: 28, TDD: 31
Antenna correlation | Low
Aggregation level and Repetition level | (24,8), (8,4), (16,4), (4,2)
Starting OFDM symbols (CFI) | 2
Frequency hopping | OFF
Number of PRB | 4 for Aggregation level = 4, 8, 16 2+4 for Aggregation level =24
Transmission type configured to UE | Distributed
DMRS scrambling sequence initialisation parameter for UE-SS | PCID = 1
Channel Estimation | DMRS based
UE residual frequency error | 50 Hz

## Slide 4: Proposals
The following test setups is for non-DRX tests.
  Propagation condition
    ETU30
  Time T1-T3 for OoS tests
    T1: 2s, T2: 0.8s, T3: 1.8s, check point: 440ms after start of T3
  Time T1-T5 for IS tests
    T1: 2s, T2: 0.8s, T3: 1.46s, T4: 0.8s, T5: 2s, check point: 0.62s after start of T5
    Note: Values can be re-visited if problem is identified during CR drafting

## Slide 5: Proposals
The following test setups is for DRX tests.
  Propagation condition
    AWGN
  Time T1-T3 for OoS tests
    Same as in Cat-0 RLM test case
  Time T1-T5 for IS tests
    Same as in Cat-0 RLM test case
  DRX configuration
    longDRX-CycleStartOffset: sf1280 for OoS and sf40 for IS
    onDurationTimer: psf10
    drx-InactivityTimer: psf1
    drx-RetransmissionTimer: psf1