## Slide 1: Way forward on UE performance requirements for FD-MIMO
Samsung,Qualcomm,MediaTek,Ericsson,Intel,LGE
3GPP TSG-RAN WG4 Meeting #78bis
San Jose del Cabo, Mexico, 11th – 15th Apr 2016
R4-163030

## Slide 2
Test applicability
  When new TM9 MU-MIMO test is introduced, Rel-13 UE that supports enhanced DM-RS is required to fulfill only Rel-13 TM9 MU-MIMO test. Legacy TM9 MU-MIMO test is not applicable to this UE.
  DMRS configuration for target UE
  Option1: dynamic changed between port {7,8,11,13} with nSCID= 0,OCC =4
  Option2: fixed as port 7, nSCID=0, OCC=4
  Option 3: fixed as port 11, nSCID=0, OCC=4
Number of interference port
  Option1: 1 port with nSCID= 0,OCC =4 (as baseline)
    Companies are encouraged to bring analysis and results in next meeting to check whether such test set-up can discriminate UE behaviour between OCC4 and OCC2 operation.
Interference port selection
  Option 1: randomized Interference port between port{7,8,11,13} except which used by input signal (target UE) as per TTI basis
  Option2: randomized interference port between port{7,8,11,13} except which used by input signal (target UE) as per TTI, per PRG basis
Beamforming modelling
  For 2 ports case (Interference + wanted signal) :Reusing existing beam-forming mode as specified in annex B.4.1
    Two 2x1 precoders randomly selected from Rel-8 layer 1 codebook (Table 6.3.4.2.3-1 in TS36.211) but not the same.
    Precoder update granularity: 1PRG per TTI
    Additional power scaling factor applied to normalize the transmit power:
PDSCH demodulation test

## Slide 3
Test Metric
  Reusing existing 8Tx PMI test metric: , is [TBD%] of the maximum throughput obtained at using the precoders configured according to the UE reports, and is the throughput measured at with random precoding.
Test applicability for CSS configuration:
  Defining performance requirements which applicable for all the CSS configurations. For each test case, select corresponding CSS configuration based on UE capability (baseline)
    FFS for detailed selection rule
    Bring simulation results for both single PMI and multiple PMI test case with different Codebook configuration 1,2,3,4 in next RAN4 meeting
Test parameters
  Introduce Single PMI test with 12 ports, (N1, N2) = (2, 3), (O1, O2) = (8, 4), CDM2, codebook configuration =1,2,3,4, PUSCH 3-1, EPA 5Hz, 64QAM ½ with rank1
  Introduce Multiple PMI test with 16 ports, (N1, N2) = (2, 4), (O1, O2) = (8, 8), CDM4, codebook configuration =1,2,3,4, PUSCH 1-2, EVA 5Hz, 16QAM ½ with rank2
Class A PMI test cases

## Slide 4
Test Metric: Reusing existing PMI test metric as relative throughout ratio between following PMI and random PMI
Test case list: 1 single PMI test case with PUCCH 1-1
Test method: Introducing test case with fading channel as EPA5Hz
Test parameters
  8Tx with Low correlation or XP High MIMO channel as baseline, further check whether applicable for FDD.
  MCS &Rank: 16QAM ½ rank1 , 64QAM ½ Rank1
Class B K=1 PMI test cases with PMI-config =1

## Slide 5
Test applicability
  In Rel-13 time frame, only introduce test case under TM9 with 1 CC
  Introduce a subset of test cases with different (K, Nmax)
    At least including (K,Nmax )= (2,8), FFS for (8,64), other possible configurations are FFS
    The detailed applicability rule based UE capability is FFS
Test methodology
  Option 1: One throughput test with single CSI-RS resource and another throughput test with multiple CSI-RS resources.
    Alt.1: Check both CRI statistics and throughput ratio between following CRI and fixed CRI.
    MCS selection and PMI selection FFS
  Other options will not be precluded.
Beamforming model
  Option 1: Dynamic power scaling
    with A = [0.8],B=1 (As example)
  Option 2: CSI-RS resource specific beamforming and beam steering channel model
Class B K>1 CRI test case

## Slide 6
Test case list
  1 test case for channel measurement restriction under TM9 with Class B K=1 with legacy codebook
  1 test case for interference measurement restriction under TM10 with Class B K=1 with legacy codebook
Test applicability
  Treating Test Case for MR –channel part as a new test case
  Depending on UE capability, once UE pass test Case for MR –interference part and then no need to pass existing TM10 static CQI test case as specified in TS36.101 9.2.4
Test metrics
  Reusing existing static CQI test metric i.e. Reporting spread of CQI value + BLER requirements (baseline)
  Other options not precluded
Test Methodology
  Interference measurement restriction test
    Option 1: Reusing test parameters for existing TM10 static CQI test as specified in TS36.101 9.2.4 with below modification:
      TP2 is blanked in even CSI-RS sub-frames
      Scheduled PDSCH will skip even CSI-RS sub-frames
      CQI reported based on odd CSI-RS sub-frames
    Other options not precluded
  Channel measurement restriction test
    Option 1: Reusing test parameters for existing TM9 static CQI test as specified inTS36.101 9.2.3 with below modification:
      Adjusting transmitted power in even CSI-RS sub-frames, Transmitted power imbalance between even CSI-RS sub-frames and other sub-frames is TBD
      Scheduled PDSCH will skip even CSI-RS sub-frame
      CQI reported based on odd CSI-RS sub-frames
    Other options not precluded
MR test

## Slide 7
Simulation assumption for PDSCH demodulation test (For information)
parameter |  | Unit | Test X
Downlink power allocation |  | dB | 0
 |  | dB | 0 (Note 1)
 |  | dB | -3
System Bandwidth |  | MHz | 10
Beamforming model |  |  | Annex B.4.1
MIMO channel |  |  | EPA5Hz, 2*2 Low
Cell-specific reference signals |  |  | Antenna ports 0,1
CSI reference signals |  |  | Antenna ports 15,…,18
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  | Subframes | 5 / 2
CSI reference signal configuration |  |  | 3
Zero-power CSI-RS configuration ICSI-RS / ZeroPowerCSI-RS bitmap |  | Subframes / bitmap | 3 / 0001000000000000
at antenna port |  | dBm/15kHz | -98
Symbols for unused PRBs |  |  | OCNG (Note 4)
Number of allocated resource blocks (Note 2) |  | PRB | 50
Rel-13-DMRS-table |  |  | Yes
MCS and Rank |  |  | 64QAM 1/2 Rank1 R.50 FDD
Simultaneous transmission |  |  | Yes
DMRS configuration for input signal |  |  | Option1: dynamic changed between port {7,8,11,13} with nSCID= 0,OCC =4 Option2: fixed as port 7, nSCID=0, OCC=4 Option 3: fixed as port 11, nSCID=0, OCC=4
DMRS configuration for interfering signal |  |  | 1 port with nSCID= 0,OCC =4 (as baseline)
Interfere port selection |  |  | Option 1: randomized Interference port between port{7,8,11,13} except which used by input signal (target UE) as per TTI basis Option2: randomized interference port between port{7,8,11,13} except which used by input signal (target UE) as per TTI, per PRG basis
PDSCH transmission mode |  |  | 9