## Slide 1: WF on 4RX PDSCH MMSE-IRC receiver
Huawei, [xx]
3GPP TSG-RAN WG4 Meeting # 78bis San Jose del Cabo, Mexico, 11 – 15 Apr 2016
Agenda Item: 6.6
R4-163035

## Slide 2: Background
Test cases of 4RX PDSCH type-A receiver had been introduced in R.13 4RX WI:
  TS36.101 section 8.10.1.1.3 (FDD) and section 8.10.1.2.3 (TDD)
    Serving cell, transmission mode TM6 rank1 with followed PMI
    One Interference cell, transmission mode TM4 with 80% rank1 and 20% rank2 probability
Compared with 2RX, 4RX UE could achieve more performance gain with IRC, in the scenarios:
  Serving cell rank >1
  Total rank of interference cell >2

## Slide 3: Way Forward
The following case(s) could be considered for 4RX UE :
  Case 1:
    Serving cell rank =2
    One interference cell
  Case 2:
    Serving cell rank=1
    Two interference cell
Companies are encouraged to provide analysis and evaluation on above cases

## Slide 4: Simulation Assumptions (for information)
  Case 1:
    Reuse the assumptions in section 8.10.1.1.3, except that
      Serving PDSCH transmission: TM4 rank2, with/without followed PMI feedback
  Case 2:
    Reuse the assumptions in section 8.10.1.1.3, except that
      Two interference cells are modelled
      The interference levels for two interference cells are the same, the INR for each cell equals to the INR which is based on DIP values in Table 8.10.1.1.3-1.
  Other cases are not precluded