## Slide 1: Motivation for new SI on Interference cancellation receiver for LTE BS
China Telecom
May, 2016
R4-163291

## Slide 2: Motivation for BS IC receiver
Importance of LTE UL throughput improvement
  With the wider usage of mobile applications like cloud services, social networking and point to point video/file sharing, UL traffic load is becoming much heavier.
Co-channel interference is a dominant limiting factor for LTE UL capacity
  BS MMSE-IRC receiver can bring in the significant gain over MMSE receiver by suppressing the inter-cell interference, in both homogeneous and heterogeneous networks, as concluded in TR 36.884 [1].
  Consider the further evolution of BS receiver, such as interference cancellation (IC) receiver, to mitigate the inter-cell interference as well as the intra-cell inter-user interference.
MMSE
MMSE-IRC
IC
BS advanced receiver
To be completed in June 2016
Proposed to be considered in Rel-14

## Slide 3: Target scenarios
Scenario 1: inter-cell interference scenario
The target cell and interference cell(s) are co-located or connected with ideal backhaul
Scenario 2: intra-cell inter-user interference scenario
Multiple users are co-scheduled on the same resource elements
  In scenario 1 and 2, full knowledge of interference parameters is available at the target cell.

## Slide 4: Potential gain by BS IC receiver (1/2)
In the inter-cell interference scenario (scenario 1), BS IC receiver is expected to achieve additional spectral efficiency gain over MMSE-IRC receiver.
 | Interference level | (DIP1, DIP2) | Average MMSE-IRC gain over MMSE *** | Potential IC gain over MMSE ****
Homogeneous scenario | Low | (-5.55, -7.09) * |  | 2.79 dB
 | Medium | (-3.17, -7.03) * |  | 4.96 dB
 | High | (-1.11, -10.91) ** | 3.1 dB for 2Rx 4.4-4.7 dB for 4Rx 4.9-5.0 dB for 8Rx | 8.40 dB
Co-channel heterogeneous scenario | Low | (-4.73, -6.67) * |  | 3.49 dB
 | Medium | (-2.08, -7.17) * |  | 7.23 dB
 | High | (-0.43, -13.78) ** | 5.5-5.9 dB for 2Rx 7.5-8.3 dB for 4Rx 8.4-8.9 dB for 8Rx | 12.81 dB
Note* DIP values simulated by China Telecom. Note** DIP values averaged among 6 companies in Rel-13 BS MMSE-IRC WI [1]. Note*** MMSE-IRC gain averaged among 7 companies in Rel-13 BS MMSE-IRC WI [1]. Note**** Assuming that the two interferers are mitigated completely. |  |  |  | 

## Slide 5: Potential gain by BS IC receiver (2/2)
  Capacity region for joint decoding indicates the performance upper band for IC receiver.
  Joint decoding: decoding of all signals is performed simultaneously.
  Capacity region for independent decoding indicates the performance upper band for MMSE receiver.
  Independent decoding: different signals are decoded independently and in parallel.
Fig. Capacity regions for a two-user M-receiver system
In the intra-cell inter-user interference scenario (scenario 2), BS IC receiver is expected to achieve noticeable spectral efficiency gain over MMSE receiver, based on the theoretical analysis [3].

## Slide 6: Proposal and scope
Proposal
  Start a RAN4-led SI in Rel-14 to study the performance benefits of BS IC receiver under typical deployment scenarios and with practical receiver implementation
Scope
  Identify the target deployment scenarios and the co-channel inter/intra-cell interference conditions
  Identify the reference receiver structures for PUSCH
  Agree on the interference models, interference levels and simulation parameters for link level evaluations
  Evaluate the link-level gain for PUSCH over baseline receiver
    Evaluate the link-level gain over baseline Rel-13 MMSE-IRC receiver for inter-cell interference scenarios.
    Evaluate the link-level gain over baseline Rel-8 MMSE receiver for intra-cell inter-user interference scenarios.
  Note: the utilization of BS IC receiver is transparent to the users, and the performance gain of BS IC receiver can also be enjoyed by legacy users.

## Slide 7: References
[1] 3GPP RP-160221, “TR 36.884 V1.0.0: Performance requirements of MMSE-IRC receiver for LTE BS”, RAN #71, Mar 2016.
[2] 3GPP RP-150206, “Revised WID: Performance requirements of MMSE-IRC receiver for LTE BS”, RAN #67, Mar 2015.
[3] Bruno Suard, Guanghan Xu, Hui Liu, et al., “Uplink Channel Capacity of Space-Division-Multiple-Access Schemes,” IEEE transactions on information theory, vol. 44, no. 4, July 1998.

## Slide 8
Thanks!