## Slide 1: Way forward on NB-IoT UE OOBB Range 3
Intel, MediaTek, ASTRI, [Nokia, Qualcomm, …]
3GPP TSG-RAN WG4 Meeting #79 R4-164467 Nanjing, China, 22 – 27 May, 2016

## Slide 2: Background (1/3)
NB-IoT is targeting small size and low cost. SAW-less receiver may be a must for low cost NB-IoT applications. To eliminate the expensive SAW filter, out-of-band blocking (OOBB) requirement should be relaxed. A SAW-less architecture will save PCB area and have lower cost.
More stringent OOBB requirement will lead to lower phase noise requirement on LO, and lower phase noise requirement will lead to much more current consumption in synthesizer. Therefore, relaxation of OOBB will also lead to low power consumption.
R4-163558 proposes Pinterference=-20dBm for NB-IoT UE OOBB range 3.
R4-164465 proposes Pinterference=-25dBm for NB-IoT UE OOBB range 3.

## Slide 3: Background (2/3)
A typical LO phase noise in low power low cost RF transceiver.
Only around 3dB lower at 85MHz offset than 60MHz offset.
@60MHz offset, PN= -145dBc/Hz
@85MHz offset, PN= -148dBc/Hz

## Slide 4: Background (3/3)
NB-IoT frequency band can be categorized into two band groups:
Low frequency band group: Band 5, 8, 12, 13, 17, 18, 19, 20, 26, 28
DL frequency range: 734~960 MHz,
High frequency band group: 1, 2, 3, 66
DL frequency range: 1805~2200 MHz

## Slide 5: Way forward on NB-IoT UE OOBB Range 3
E-UTRA band | Parameter | Units | Frequency |  | 
 |  |  | Range 1 | Range 2 | Range 3
 | Psignal | dBm | REFSENS+6dB | REFSENS+ 6 dB | REFSENS+ 6 dB
 | PInterferer | dBm | -44 | -30 | -15
1, 2, 3, 5, 8, 12, 13, 17, 18, 19, 20, 26, 28,66 | FInterferer (CW) | MHz | FDL_low -15 to FDL_low -60 | FDL_low -60 to FDL_low – 85 | FDL_low – 85 to 1 MHz
 |  |  | FDL_high +15 to FDL_high + 60 | FDL_high + 60 to FDL_high + 85 | FDL_high + 85 to +12750 MHz
NOTE 1: For band 5, 8, 12, 13, 17, 18, 19, 20, 26, 28 , the power level of the interferer (PInterferer) for Range 3 shall be modified to -20 dBm for FInterferer > 284 MHz and FInterferer < 1410 MHz.
NOTE2: For band 1, 2, 3, 66, the power level of the interferer (PInterferer) for Range 3 shall be modified to -25dBm for FInterferer > FDL_low - 200MHz and FInterferer < FDL_high + 200MHz.
Proposal: adopt the following table with note