## Slide 1: Way forward on UE performance enhancement under SFN scenario
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #80 R4-165377
Gothenburg, Sweden, 22-26 Aug, 2016

## Slide 2: Background
The initial simulation assumptions were agreed in 78bis meeting, and down selection is needed for some assumptions.
Baseline option given in R4-163052 was agreed as the SFN channel model for defining requirements.
Three options for reference receiver were included, and down selection is needed to define requirements.

## Slide 3: Requirements for advanced UE
Define requirements for advanced UE based on 4-taps channel model referred in WF(R4-163419) agreed in #79 meeting.

## Slide 4: Test case and parameters
Define two test cases for UE demodulation performance
  Case 1: Ds=1000m,Dmin=300
  Case 2: Ds=500m,Dmin=5
  MCS
  MCS=19 for Case 1 and Case 2
  SNR definition for Case 2
  Normalized SNR

## Slide 5: Reference receiver
Define UE demodulation requirements based on the alternative 1 receiver in WF(R4-163419).
  Alternative 1: UE assuming extended U-shape Doppler spectrum and always covering the high power paths in Doppler spectrum

## Slide 6: CSI test
Introduce CSI test for advanced UE based on 4-taps channel model.