## Slide 1
3GPP TSG-RAN WG4 #80
Gothenburg, Sweden, 22 - 26 Aug, 2016
Agenda item: 8.11.4
LG Electronics
WF on V2V RRM core requirement
R4-165611

## Slide 2: Way Forward
UE transmission timing
  eNB as timing reference (IC)
    TA : NTAoffset=0, NTA,SL=0
    TE : Reuse the existing requirement
  GNSS as timing reference (IC, OoC)
    TA : NTAoffset=0, NTA,SL =0
    TE : +/- 12 Ts
  SyncRef UE as timing reference (OoC)
    Reuse the existing requirement in OoC

## Slide 3: Way Forward
Selection/Reselection of Sync Reference
  SyncRef UE (OoC)
    Tdetect,SyncRef UE is defined as 3 seconds at SCH Es/Iot ≥ -3 dB, provided that the V2V UE is allowed to drop a maximum of 14% of its transmissions at the physical layer for the purpose of SyncRef UE selection / reselection.

## Slide 4: Way Forward
Initiation/Cease of SLSS transmissions
  eNB based SLSS (IC)
    Reuse the existing requirement
  SyncRef UE based SLSS (OoC)
    400ms

## Slide 5: Way Forward
Measurement for resource selection/reselection
  The UE physical layer shall be capable of performing the [S-RSSP] measurements and/or the [S-RSSI] measurements within one subframe on resource allocations are indicated by higher.
  The [S-RSRP] measurement performed according to this section shall meet the [S-RSRP] measurement accuracy requirement in Section 9.10.2.
  The [S-RSSI] measurement performed according to this section shall meet the [S-RSSI] measurement accuracy requirement in Section [TBD].