## Slide 1: Way forward on supported RF configurations for NB-IoT
Huawei, CMCC, Ericsson, Nokia, NTT DOCOMO
3GPP TSG-RAN WG4 Meeting #80 R4-166372
Gothenburg, Sweden, 22 – 26 August 2016

## Slide 2: Reference
[1] R4-79AH-0063, “BS conformance tests: Manufacturer declaration”, Ericsson
[2] R4-79AH-0198, “General consideration for NB-IoT BS conformance test”, Huawei
[3] R4-79AH-0203, “Overview on 37.141 conformance testing”, Huawei

## Slide 3: WF for TS 36.141
For TS 36.141, the following RF configurations should be specified.
  NB-IoT standalone
  E-UTRA + NB-IoT in-band
  E-UTRA +NB-IoT guard band
  E-UTRA + NB-IoT in-band +NB-IoT guard band
The following RF configuration should be specified or not shall be based on operator input on deployment scenarios and decision will be make in RAN4#80.
  E-UTRA + NB-IoT Standalone

## Slide 4: WF for TS 37.141
For TS 37.141 new supported RF configurations, the following new RAT Capability Set (CS) shall be added to support NB-IoT standalone.
  CS8: GSM + NB-IoT standalone
  CS9: UTRA + NB-IoT standalone
  CS10: E-UTRA + NB-IoT standalone
  CS11: GSM +UTRA + NB-IoT standalone
  CS12: GSM+ E-UTRA + NB-IoT standalone
  CS13: UTRA + E-UTRA + NB-IoT standalone

## Slide 5: WF for TS 37.141
It is proposed to update the existing CSs (CS2, CS3, CS5) that support E-UTRA today to support NB-IoT in-band and/or guard band operation. The support of NB-IoT in-band and/or guard band operation is optional and shall be declared by the manufacturer.
Capability Set supported by the BS | CS2 | CS3 | CS5
Supported RATs | E-UTRA (MC), NB-IoT in-band**, NB-IoT guard band*** | UTRA, E-UTRA, NB-IoT in-band**, NB-IoT guard band*** | GSM, E-UTRA, NB-IoT in-band**, NB-IoT guard band***
NOTE**: The support of NB-IoT in-band operation is optional and declared by the manufacturer. NOTE***: The support of NB-IoT guard band operation is optional and declared by the manufacturer. |  |  | 

## Slide 6: WF for TS 37.141
The following Capability Set (CS) should be specified or not shall be based on operator input on deployment scenarios and decision will be make in RAN4#80.
  CS14: E-UTRA + UTRA + GSM + NB-IoT standalone
  updating the existing CS6 and CS7 that support E-UTRA today to support NB-IoT in-band and/or guard band operation.

## Slide 7
CS | UTRA(MC) | E-UTRA(MC) | GSM | NB-IoT |  | 
 |  |  |  | In-band | Guard-band | Stand-alone
1 | YES |  |  |  |  | 
2 |  | YES |  | (YES) | (YES) | 
3 | YES | YES |  | (YES) | (YES) | 
4 | YES |  | YES |  |  | 
5 |  | YES | YES | (YES) | (YES) | 
6(?) | YES | YES | YES | (YES) | (YES) | 
7(?) | YES | YES | YES | (YES) | (YES) | 
8 |  |  | YES |  |  | YES
9 | YES |  |  |  |  | YES
10 |  | YES |  |  |  | YES
11 | YES |  | YES |  |  | YES
12 |  | YES | YES |  |  | YES
13 | YES | YES |  |  |  | YES
14(?) | YES | YES | YES |  |  | YES
For information