## Slide 1: Way forward on ACLR and ACS modelling for the ITU WP5D simulations
R4-166719

## Slide 2: ACLR modelling
“Flat ACLR” is assumed in the spatial domain
  This means that it is assumed that the adjacent channel emissions are beamformed by the aggressor transmitter in exactly the same way as the aggressor wanted signal, such that their ratio does not vary in space.
  The underlying assumption is 100% correlation in unwanted emissions between transmitters
Disclaimers:
  “Flat ACLR” refers to the spatial domain only, not the frequency domain
  This assumption is for the ITU simulations only; further discussion is needed to clarify the impact or lack thereof of unwanted emissions correlation on requirements metrics .
  Assuming a flat ACLR for the ITU-simulations does not imply that it is proven that adjacent channel emissions are correlated with real transmitters
  Assuming a flat ACLR for the ITU simulations does not imply agreement that this scenario is somehow a “worst case” for co-existence
    Some companies have presented simulations suggesting that the spatial pattern of ACLR does not impact co-existence. Other companies are checking these simulations and running own simulations

## Slide 3: ACS modelling
[“Single ACS” is assumed in the spatial domain] – TBC to RAN4#80bis
  This means that it is assumed that RX beam pattern is the same for both the wanted and adjacent channels in all directions
Disclaimers
  “Spatial ACS” refers to the spatial domain only, not the frequency doman
  This assumption is for the ITU simulations only; further discussion is needed to clarify the impact or lack thereof of ACS spatial pattern on requirements metrics.
  Assuming a flat ACS for the ITU-simulations does not imply that it is proven that ACS is always flat in real receiver arrays
  Assuming a flat ACS for the ITU simulations does not imply agreement that this scenario is somehow a “worst case” for co-existence
  There is an implicit assumption that the aggressor RX power is within the dynamic range of the receiver (i.e. is not a blocker) and hence the beamforming pattern holds

## Slide 4: ACIR calculation
Under the assumption of flat ACLR and flat ACS, ACIR at a UE is calculated as follows:
* *
Where
  Gt() is the directional array gain of the aggressor considering the aggressor beam pattern and the direction of the victim UE from the aggressor
  ) is the directional array gain of the UE considering the UE beam pattern and the direction of the aggressor from the victim UE.
  “Array gain” includes both antenna element and array beamforming gain
  is the absolute level of aggressor interference at the receiver
  is the conducted transmitter power of the aggressor
  Pathloss is the pathloss between the agressor and victim.
    There will be a minimum limit to pathloss, based on minimum distance or similar