## Slide 1: Blind Detection Conclusions on MUST Case 3
MediaTek
3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22nd -26th August 2016
Agenda Item: 8.19.2
R4-166793

## Slide 2: Way Forward
In CRS-based TMs,
  Interference existence detection is not feasible
    Performance degradation is observed in legacy SU-MIMO scenario due to non-zero blind detection error rate
  Given interference present, given interference existence signaled and practical detection algorithm, the degradation at 10% BLER of the ideal performance is summarized in the table in the next page

## Slide 3: Way Forward
 | Modulation combination {target, interference} | Throughput degradation at 90% throughput of ideal performance |  | 
 |  | Detecting precoder, signaling modulation | Detecting modulation, signaling precoder | Detecting both precoder and modulation
4TX | {QPSK, QPSK} | 2% | 2% | 4%
 | {QPSK, 16QAM} | 2% | 2% | 4%
 | {QPSK, 64QAM} | 2% | 2% | 4%
 | {16QAM, QPSK} | 16% | 5% | 25%
 | {16QAM, 16QAM} | 11% | 6% | 25%
 | {16QAM, 64QAM} | 11% | 7% | 19%
 | {64QAM, QPSK} | 60% | 21% | 76%
 | {64QAM, 16QAM} | 47% | 18% | 58%
 | {64QAM, 64QAM} | 47% | 13% | 56%
2TX | {QPSK, QPSK} | < 1% | 2% | 5%
 | {QPSK, 16QAM} | 1% | 3% | 5%
 | {QPSK, 64QAM} | < 1% | 3% | 5%
 | {16QAM, QPSK} | 12% | 5% | 23%
 | {16QAM, 16QAM} | 15% | 10% | 27%
 | {16QAM, 64QAM} | 20% | 15% | 31%
 | {64QAM, QPSK} | 32% | 26% | 59%
 | {64QAM, 16QAM} | 35% | 15% | 47%
 | {64QAM, 64QAM} | 43% | 18% | 49%

## Slide 4: Way Forward
In DMRS-based TMs,
  Interference existence detection is not feasible in terms of UE’s blind detection complexity.
    There are too many hypotheses, considering the combinations of scrambling ID, DMRS port and OCC length.
  FFS on the blind detection performance on modulation, given the existence of interference signaled.