## Slide 1: Way forward on MIB acquisition delay in eMTC
Qualcomm, Intel
3GPP TSG-RAN WG4 Meeting #80
Göteborg, Sweden 22-26 August, 2016
R4-166836

## Slide 2: Background
In RAN4 #80, it was identified that In Rel-13 eMTC, MIB acquisition delay impacts core and performance requirements – both in CE mode A & mode B [R4-166822]
MIB Acquisition delay needs to be evaluated when repetition of PBCH (as agreed in Rel-13 eMTC) is enabled
Coverage level of CE mode A is nominally assumed to be -6dB and CE mode B to be -15dB, hence MIB acquisition delay needs to be evaluated at SNR = -6dB and SNR = -15dB

## Slide 3: MIB acquisition
MIB TTI = 40ms
Candidate algorithms to acquire MIB
  Baseline: The “keep trying” decoder is definition is: The decoder simply “keeps trying” to decode the transmitted Rel-13 eMTC PBCH frames until the decoder eventually gets lucky and decodes it correctly. With this solution there is a trade-off between coverage gain and decoding time (i.e. the number of decoding attempts). [Refer to R1-132908]
  Other algorithms are not precluded
MIB acquisition delay = [90]%-ile of the number of frames required to successfully decode the MIB
To obtain MIB acquisition delay, companies are encouraged to provide CDF of MIB acquisition time based on the simulation results in the next slide

## Slide 4: Simulation assumptions
Parameter | Case 1 | Case 2 | Case 3 | Case 4
Sys BW | 10MHz | 10MHz | 10MHz | 10MHz
Duplex Mode | FDD | FDD | TDD | TDD
Channel | EPA1 | ETU1 | EPA1 | ETU1
SNR | Mode A: -6dB Mode B: -15dB |  |  | 
Repetition of PBCH | Enabled |  |  | 
Antenna Configuration & Correlatiom | 2x1 low |  |  | 
UE frequency error | 100Hz |  |  | 
For Mode A, companies are encouraged to provide simulation data with higher doppler frequency also, e.g. EPA5, ETU30