## Slide 1: Way forward on open issues for eMTC UE demodulation requirements
Huawei, HiSilicon, Ericsson
3GPP TSG-RAN WG4 Meeting #80
Göteborg, Sweden 22-26 August, 2016
R4-166997

## Slide 2: Scheduling pattern for PDSCH TM9 and TM2 with repetition
Interesting companies are encouraged to propose the scheduling pattern for PDSCH tests:
  Option 1: Reduce noise power on MPDCCH subframes to reduce MPDCCH repetition number to 1.
  Option 2: Set enough repetition number for MPDCCH to ensure 100% of decoding
  Option 3: Apply power boosting for MPDCCH to ensure 100% of decoding
  Option 4: Other options are not precluded.

## Slide 3: PDSCH demodulation requirements
Interesting companies are encouraged to provide the simulation results and to propose the TBS/repetition combination for FDD and TDD including impairment error in RAN4#80bis.
TBS and repetition number for TM9 in CE Mode A
  Option 1: 152bits and 2 repetition (SNR=-5.7dB)
  Option 2: 504bits and 8 repetition (SNR=-3.3dB)
  Option 3: 504bits and 16 repetition (SNR=-6.4dB)
  Note: The SNR values above are based on the ideal simulation results

## Slide 4: Scheduling pattern for PDSCH TM6 test and CQI definition test (No repetition)
Option 1: 10ms periodicity, 5ms for DL, 1ms gap, 3ms for UL, 1ms for gap
Option 2: 8ms periodicity, 1ms for MPDCCH, 1ms for gap, 1ms for PDSCH, 1ms gap, 3ms for UL, 1m for gap