## Slide 1: 3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22 - 26 Aug, 2016
Intel, Ericsson
Way Forward on NPBCH Coverage Study
R4-167117

## Slide 2: Background
RAN4 observes an approximately 4 dB gap between the target SNR points for NPBCH and NPDCCH demodulation performance requirements.
RAN4 performance observation have been captured in R4-165521. The results cannot verify NPBCH coverage.

## Slide 3: Verification on NPBCH Coverage
Interested companies provides NPBCH performances evaluated under ETU-1Hz and EPA-1Hz at SNR=-12dB.
Test scenarios are given in Table-1 in R4-165352.

## Slide 4: NPBCH Coverage Shortage Investigation
Consider “keep trying” UE behavior on NPBCH performance without any combining across TTI.
  Define keep trying window length, W
  For reference, “keep trying” was defined for eMTC in R1-132908
Probability error of “keep trying” UE
  P( NBPCH error) = ‘W’ consecutive NPBCH error.
  W= [ 1, 2, 3, … ] ?

## Slide 5: NPBCH Coverage
For the final requirement, capture NPBCH performance at SNR=-12, which is aligned with the extended coverage requirement.
  Capture “trying window length W” as requirement reference of Max NPBCH Acquisition Time.

## Slide 6: Evaluation on Coverage
  For coverage evaluation, discuss further on both Probability of NPBCH error rate and acquisition time.
  For example …
NPBCH Decoding Tries | Max NPBCH Acquisition Time | NPBCH Error rate | Coverage
1 | 640ms | X % | - 12 dB
2 | 1.28s ( 2* 640ms ) | Y % | - 12 dB
3 | 1.92s ( 3* 640ms ) | Z % | -12 dB