## Slide 1: Way Forward on NR UE Testability
Intel Corporation, CATR
3GPP TSG-RAN WG4 Meeting #80bis R4-167278
Ljubljana, Slovenia, 10-14 August, 2016

## Slide 2: Background
With a clearer understanding of the UE RF parameters, discussions on NR testability have progressed in RAN4

## Slide 3: Agreements (1)
General test methodology for UE RF at high frequency (f > TBD GHz)
  OTA measurements are the baseline configuration for testing all UE RF parameters
  Possible approaches include far-field, near-field, or others
  Test equipment vendors are encouraged to provide their analysis of feasibility and Pros/Cons across the possible approaches and at least between far-field and near-field approaches by RAN4 #81
How to control the DUT
  Companies are encouraged to provide proposals on test interface definitions and to identify potential high-level input to other WGs
Possible test metrics in the next slides are intended to encourage further study; other possible test metrics are not precluded
Companies are encouraged to prioritize the discussion on maximum TX power and REFSENS for the next meeting

## Slide 4: Possible test metrics for further study (1)
RF requirement | Test metric baseline for study | Test setup notes baseline for study
Max output power, Min output power | Opt.1: EIRP Opt.2: TRP | Opt.1: Far-field measurement of EIRP in a single beam direction Opt.2: Far-field measurement of EIRP over N beam directions Opt.3: TBD
ON/OFF time mask, power control, PCMAX | Opt.1: EIRP Opt.2: TRP | Opt.1: Far-field measurement of EIRP in a single beam direction Opt.2: Far-field measurement of EIRP N beam directions Opt.3: TBD
Frequency error, EVM | TBD | 
Unwanted emissions (SEM, IB, OOB, spurious, ACLR) | Opt.1: TRP Opt.2: EIRP | Test time of each approach should be investigated Current conducted approach is analogous to TRP Selection of EIRP approach may imply a potentially inappropriate and over stringent definition of unwanted emissions metric due to inclusion of BF gain of unwanted emission
Tx OFF power | Opt.1: TRP Opt.2: EIRP | Test time of each approach should be investigated With Tx OFF, UE does not form a beam; EIRP over N DUT orientations may be sufficient. The difference between EIRP and TRP would then be basically whether a max or average is taken.
Transmit intermodulation | TBD | 
Occupied BW | Opt.1: EIRP Opt.2: TRP | Opt.1: Far-field measurement of EIRP in a single beam direction Opt.2: Far-field measurement of EIRP N beam directions Opt.3: TBD
NOTE: The possible test metrics are based on preliminary study and can be revisited in future study.

## Slide 5: Possible test metrics for further study (2)
RF requirement | Test metric baseline for study | Test setup notes
REFSENS | Opt.1: EIS Opt.2: TRS | Opt.1: Far-field measurement of EIS in a single beam direction Opt.2: Far-field measurement of EIS over N beam directions Opt.3: TBD
Max input level | Opt.1: EIS Opt.2: TRS | Opt.1: Far-field measurement of EIS in a single beam direction Opt.2: Far-field measurement of EIS over N beam directions Opt.3: TBD
ACS, Blocking (IBB, OOB, NBB) | Opt.1: TRS Opt.2: EIS with blocker and signal aligned Opt.3: EIS with blocker and signal from different directions | Test time of each approach should be investigated. Current conducted approach is analogous to TRS. Selection of EIS with blocker and signal aligned approach may imply a potentially inappropriate and over stringent definition of blocking metric due to inclusion of BF gain of unwanted signal
NOTE 1: Intermodulation, spurious response, spurious emissions, and receiver image tests are FFS
NOTE 2: The possible test metrics are based on preliminary study and can be revisited in future study.

## Slide 6: Open issues
A further level of detail is needed
  Test setup descriptions
  Test setup dimensions
  Potential restrictions on the DUT (such as size, positioning, etc.)
  High-level descriptions of sources of measurement uncertainty
Clear definitions for abbreviations and terminology are needed
Possible approaches for thermal testing are recommended for further discussion

## Slide 7: References
[1] R4-167212, “Conformance testing of beamforming characteristics,” ROHDE & SCHWARZ
[2] R4-168320, “UE Conformance Testing for mmWave,” Qualcomm Incorporated
[3] R4-167413, “Consideration on UE HF output power and REFSENS,” Huawei, HiSilicon
[4] R4-168410, “UE RF requirements in mmWave,” NTT DOCOMO, INC.
[5] R4-168454, “Consideration to EIRP/EIS in mm Wave,” NTT DOCOMO, INC.
[6] R4-168324, “Spurious emission band UE co-existence in mmWave,” NTT DOCOMO, INC.
[7] R4-168318, “On UE EIS Determination,” Qualcomm Incorporated
[8] R4-168050, “Blockers in the mm-wave band,” Qualcomm Incorporated
[9] R4-168392, “NR blocking requirements for mmWave,” Huawei, Hisilicon
[10] R4-168394, “Consideration of ACS/blocking in mm Wave,” NTT DOCOMO, INC.
[11] R4-167277, “UE testing interface for NR RF," Intel Corporation, CATR
[12] R4-168558, "Special conformance test functions for 5G testability," Keysight Technologies UK Ltd