## Slide 1
3GPP TSG-RAN WG4 Meeting #80bis R4-168490
Ljubljana, Slovenia, 10 - 14 Oct, 2016
Agenda item: 8.15.1
Document for: Approval
UE capability for UL256QAM
KDDI Corporation

## Slide 2: Background/Proposals
In RAN4#80, it was extensively discussed whether UL256QAM feature would be supported per UE or per band (groups).
This contribution tries to show KDDI’s position on this topic.
KDDI proposes to support UL256QAM feature per band or band groups not per UE.

## Slide 3: Justification
    <Assumption>
      Today’s smart phone supports a number of frequency bands within single device. Let’s imagine 25 bands are supported as an example.
    <Per UE support option>
      UE vendors are mandated to test all of bands. This is not cost effective because there would be no operator in the world which possesses 25 bands’ spectra.
      If one of 25 bands fails requirements regarding UL256QAM, UE vendor has to change its design. This is also not cost effective approach.
    <Per band support option>
      UE implementation cost can be optimized.
      One of possible concerns for this option is that UL256QAM is not supported in certain operators’ band.

## Slide 4: Possible compromise
Introduce band groups. Below is just one of examples (contents in this slide is not for approval).
# of group | Frequency Range | 3GPP bands
Group#0 | Below 1GHz | 5, 6, 8, 12, 13, 14, 17, 18, 19, 20, 26, 27, 28, 31, 44, 68
Group#1 | 1 – 1.694 GHz | 11, 21, 24, 45
Group#2 | 1.695 – 2.7 GHz | 1, 2, 3, 4, 7, 9, 10, 23, 25, 30, 33, 34, 35, 36, 37, 38, 39, 40, 41, 65, 66, 70
Group#3 | 2.7 – 3.8 GHz | 22, 42, 43
Group#4 | 3.8 – 6 GHz | 46, 47 (NOTE: B46 will support UL by eLAA)
Group#5 – 7 | Reserved for future extension | N/A