## Slide 1: Way forward on UE and BS NF for mm-waves and ITU-R related work
Agenda Item: 10.5.1
Document for: Approval
Source: Ericsson, Sony
3GPP TSG-RAN WG4 #80bis Tdoc R4-168531
Ljubljana, Slovenia, 10th – 14th October 2016

## Slide 2: Background
The Noise figure for mm-wave frequencies has been extensively discussed in R4-166526 and R4-168530.
  The Noise Figure is not given by the LNA alone, but also by, bandwidth and dynamic range dependencies as there is a delicate balance .
Beside LNA, typical noise figure contains additional losses due to switches, filters, routing losses, packaging loss, etc (along with some additional margins)
For specification related work in future, full receiver chain, complex relation between noise figure, dynamic range, bandwidths and heat dissipation should be considered.

## Slide 3: Way forward
Proposal 1: The principles outlined below are essential when deriving the Noise Figure (NF) values for mm-waves and should be considered for the mm-waves and ITU-R related work in RAN4.
  The Noise Figure is not given by the LNA alone, but also by, bandwidth and dynamic range dependencies as there is a delicate balance .
  The requirement levels should be carefully adapted to the reasonable levels that the technology can provide in order to facilitate array antennas with many elements.
  Due to compact and highly integrated building practice needed for mm-wave systems with many transceivers and antennas, careful and often complex consideration regarding the power efficiency and heat dissipation in small area/volume is necessary.
  A full receiver chain all the way up to radiating elements should be addressed as all parts in the chain would contribute to the overall receiver performance.

## Slide 4: Way forward (contd.)
Proposal 2: The NF for both BS and UE should be defined as same value for the ITU-R related work.
  It is assumed that the performance differ less between UE and BS for mm-waves on transceiver level compared to lower frequencies below 6 GHz but also recognized that different topologies between UE and BS could result in larger difference in performance.
    in particular for different UE implementation, the mm-wave antennas could be spread over the physical available area resulting in possibly higher routing losses.
  The possible difference between UE and BS performance should be carefully considered during the requirement development phase but as we have very limited time before the ITU-R response, RAN4 should use same typical NF values for UE and BS for the RAN4 co-existence studies as well as ITU-R related compatibility parameters.

## Slide 5: Way forward (contd.)
It is proposed to adopt the following typical NF values for UE and BS for mm-wave example frequencies of 30 , 45 and 70 GHz for ITU-R WP5D related coexistence simulations work in RAN4:
  Proposal 3: The typical BS noise figure for 30 GHz should be set to 9 dB.
  Proposal 4: The typical UE noise figure for 30 GHz should be set to 9 dB.
  Proposal 5: The typical BS noise figure for 45 GHz should be set to 11 dB.
  Proposal 6: The typical UE noise figure for 45 GHz should be set to 11 dB.
  Proposal 7: The typical BS noise figure for 70 GHz should be set to 13 dB.
  Proposal 8: The typical UE noise figure for 70 GHz should be set to 13 dB.