## Slide 1: Way forward on CSI reporting performance under SFN scenario
Huawei, HiSilicon, MediaTek,
CMCC, NTT DOCOMO ,CATT,
3GPP TSG-RAN WG4 Meeting #80 bis R4-168665
Ljubljana, Slovenia, 10 - 14 Oct 2016

## Slide 2: Background
The CSI part of the high speed enhancement WI was identified as follows,
  Specify new CSI requirements considered for the final solutions to enhance the downlink demodulation performance if needed.

## Slide 3: Discussion on CSI Test Introduction
RAN4 firstly verifies needs and feasibility of the HST CSI Test Introduction based on the evaluation results.
Page 4~6 is for Information.

## Slide 4: Simulation assumption
  Scenario: Dmin=1000m, Ds=50m.
SNR definition: normalized SNR
CQI reporting interval: 5/10 ms

## Slide 5: CQI test metric
Option 1:Use TP2/TP1 with option 1 definition as the test metric to distinguish legacy and advanced UE.
    TP1: throughput performance with follow CQI during 1000m~1100m region in the SFN scenario channel model;
    TP2: throughput performance with follow CQI during 1000m~2000m region in the SFN scenario channel model.
Option 2:The reported CQI values shall be in the range of +-1 of the reported median more than [90]% of the time.
Option 3:The existing frequency non-selective fading test method can be considered for CQI reporting on high speed.
Other options are not precluded

## Slide 6: For information
Encourage companies to provide the analysis and evaluation about the CQI test.
The feasibility of defining the CQI test should be based on the results.
  Variation of the reporting CQI index
    The trajectory can be provided.
  Performance( reporting CQI distribution and throughput ) gap between legacy UE and advanced UE.