## Slide 1: WF on eMTC CEMode B RLM test
Nokia, Alcatel-Lucent Shanghai Bell, Qualcomm, Ericsson
R4-168692
3GPP TSG-RAN WG4 Meeting #80bis
Ljubljana Slovenia, October 10 – 14, 2016
Agenda Item: 6.1.1

## Slide 2: Background
RAN4 has discussed RLM test for eMTC CEMode B, and agreed WF on testing methodology in RAN4#80 in R4-167030. In RAN4#80bis, the template structure of the test case was captured in R4-178679.
There are still some technical open issues before test cases can be finalized. They will be addressed in the next slides.

## Slide 3: Test setup
The combination of aggregation level and repetition (AL,R) used for the hypothetic MPDCCH transmission is
  Set 1: (16, 256) for Qout and (4,128) for Qin for OoS test cases
  Set 2: (16, 128) for Qout and (4,64) for Qin for IS test cases
Propagation condition considered for the test cases are to be select from
  AWGN
  ETU30
  Companies are encouraged to provide simulation results on Qin and Qout values for the two sets of combinations.
  Based on the results, RAN4 may drop the CEMode B test if a test setup which meets below conditions cannot be found
  sufficient gap between Qin and Qout, and
  meaningful SNR difference compared to that in CEMode A test
  other combination of (AL,R) is not precluded if Set 1 and Set 2 cannot meet the above conditions

## Slide 4: MPDCCH simulation assumptions
Parameter | M-PDCCH (CE Mode B)
DCI format | DCI Format 6-1B
System Bandwidth | 10 MHz
Channel model | AWGN, ETU30
Antenna configuration | 2x1
Number of information bits (incl. 16 bits CRC) | 18
Antenna correlation | Low
Aggregation level and Repetition level | (16,256), (4,128), (16,128), (4,64)
Starting OFDM symbols (CFI) | 2
Frequency hopping | OFF
Number of PRB | 4 for Aggregation level = 4, 8, 16 2+4 for Aggregation level =24
Transmission type configured to UE | Distributed
DMRS scrambling sequence initialisation parameter for UE-SS | PCID = 1
Channel Estimation | DMRS based
UE residual frequency error | 50 Hz

## Slide 5: General open issues
Companies are encouraged to provide inputs on the following open issues
  Time durations used in the tests
  Time period to allow gradual change in SNR
  Repetition and aggregation level for MPDCCH used for scheduling
  Configuration of repetitions for PUSCH transmission