## Slide 1: WF on eMTC UE demodulation and CQI
Ericsson, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #80bis
Ljubljana, Slovenia, 10-14, October, 2016
R4-168697

## Slide 2: Scheduling pattern for CE mode A without repetition
Option 1: 10ms periodicity, 5ms for DL, 1ms gap, 3ms for UL, 1ms for gap
Option 2: 8ms periodicity, 1ms for MPDCCH, 1ms for gap, 1ms for PDSCH, 1ms gap, 3ms for UL, 1ms for gap

## Slide 3: MPDCCH scheduling during PDSCH test
Set enough repetition number for MPDCCH to ensure [99.9]% of decoding with [3]dB power boosting of MPDCCH transmission
  Rep=[8] for TM9
  Rep=[32] for TM2

## Slide 4: MPDCCH/PDSCH demodulation requirements
Companies are encouraged to provide the results with impairments by RAN4#81 for both FDD/HD-FDD and TDD to set the requirements.

## Slide 5: PBCH demodulation requirement
Interesting companies are encouraged to provide the proposal how to specify the PBCH demodulation requirements together with the results with impairments.
  Option 1: Specify PBCH demodulation requirements with 1% BLER with the assumption PBCH decoding is performed every 40ms.
    Same definition as the existing LTE PBCH demodulation requirements.
  Option 2: Specify PBCH demodulation requirements with 1% BLER with the assumption PBCH decoding is performed every W x 40ms. W is integer > 1.
  Option 3: Other options are not precluded

## Slide 6: CQI definition test
Interesting companies are encouraged to provide the simulation results to finalize the requirement in RAN4#81

## Slide 7: UE-selected subband CQI test
Test points:
  [5]/[6]dB.
Set the gamma for Cat-M1 UE-selected subband CQI test to TBD.
Interesting companies are encouraged to provide the simulation results to decide the throughput ratio (gamma) and to finalize the requirement in RAN4#81