## Slide 1: Way forward on eLAA TX requirements
Agenda item 8.18.2
Ericsson
R4-1610836
3GPP TSG-RAN WG4 Meeting #81
Reno, NV, USA, 14 – 18 December 2016

## Slide 2
WF based on the RAN#81 Evening Adhoc on eLAA

## Slide 3: Maximum output power and tolerance
23 dBm +2/-3 dB for the CA configurations

## Slide 4: MPR
One number for full allocation, and one for partial allocation (per modulation)
Partial allocation: [2.5-3] dB for QPSK, [3] dB for 16QAM, [4] dB for 64QAM

## Slide 5: NS values and associated requirements
Consider A-MPR and additional requirements for UNII-3 in addition to 5150-5350 MHz and 5470-5725 MHz
Europe
  [no further requirements identified]
Japan
  [discussion on the Japanese spectrum mask] Not use an occupied bandwidth less than 20 MHz for eLAA
US
  Add UNII-3 emissions requirements

## Slide 6: A-MPR
Europe
  Differentiation between smaller and larger allocations, modulation dependent
Japan
  same A-MPR for the Japanese and European requirements? (for the NS indicated in Japan) recognising that ACLR2 is not an issue and that the Japanese mask is not more stringent than the ETSI [mask]
US
  A-MPR specified for all channels in 5150-5350 and 5470-5725 MHz against the relevant requirements (-41 dBm/MHz, -27 dBm/MHz and the PSD requirements)
    Specify A-MPR for the channels adjacent to the band edge where -41 dBm/MHz applies