## Slide 1: WF on MUST performance tests
MediaTek
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13th - 17th February 2017
Agenda Item: 7.28.1
R4-1700894

## Slide 2: Way Forward
MUST Case 1 and Case 2,
  No new test on far UE in MUST Case 1 and 2.
  No additional test for starting OFDM symbol.
  Introducing following 3 test cases for MUST Case 1 and Case 2
    Test A1: TM2, 64QAM, with p-a-must. Both UEs are rank-1
    Test A2: TM3, QPSK, without p-a-must. Both UEs are rank-2
    Test A3: TM4, 16QAM without p-a-must. MUST-near UEs is rank-2, and MUST-far UE is rank-1
  Companies are encouraged to provide views on the following parameters
    MCS, p-a, p-a-must, power ratio, … etc.

## Slide 3: Way Forward
MUST Case 3,
  Introducing the following 3 test cases for MUST Case 3
    Test B1: TM8/9, k-max =1, BMUST = 2, 2Rx
    Test B2: TM9, k-max =3, BMUST = 6, 4Rx
    Test B3: TM9/10, k-max =1, BMUST = 4, 2Rx
    where BMUST is the number of additional bits added in the extended DCI formats
  The number of interference layers is 1 in Test B2.
  RAN4 to first focus on 2Rx performance requirement of Test B1 and Test B3
  Companies are encouraged to provide views on the following parameters
    Tx antenna number, TM, MCS, precoder… etc.