## Slide 1: On spectral utilization and EVM for NR
Agenda item: 10.4.1.1
Document for: Approval
Source: Orange
R4-1701760
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13 - 17 February, 2017

## Slide 2: background
The spectral utilization (SU) has been extensively studied for f-OFDM and Windowed Overlapped Add (WOLA).
The previous studies show that f-OFDM can achieve better SU than WOLA, e.g. for 10 MHz carrier bandwidth, f-OFDM can reach 97.2% SU [1]
WOLA can improve SU by increasing the window length [2] however this will reduce the protection for multi-path propagation [3]
WOLA has advantages in terms of latency and complexity.
In the “LS on NR waveform”, RAN1 agreed that additional pre-processing techniques on top of CP-OFDM are not precluded [4]
In this contribution, we present a possible enhancement for WOLA to increase SU for WOLA without the need of increasing window length
[1] R4-1609411, Further discussion on spectrum utilization, Huawei, HiSilicon
[2] R4-1609647, F-OFDM vs WOLA for Guardband, Qualcomm Incorporated
[3] R4-1609945, Further elaboration on NR guard, Ericsson
[4] R4-167218, LS on waveform NR, RAN1

## Slide 3: Study assumptions
Single numerology in downlink case, carrier bandwidth 10 MHz
Rapp PA model is considered
SE is estimated with theoretical Shannon capacity
f-OFDM with 50% filter length
WOLA with 2% window length

## Slide 4: EVM and PSD for WOLA
Pros:
  constant EVM  no edge issue
Cons:
  with 2% window, marginal SU improvement is obtained (< 1%)
Conclusion: WOLA with 2% window length can difficultly have better SU than LTE

## Slide 5: SU improvement for WOLA
Use spreading method at the edge PRBs (in green) can increase the overall SU and SE
spreading method: repeat & reverse sign at each pair of subcarriers
1
2
3
4
49
50
5
PRB index
53
54
51
52
a
-a
b
-b
c
-c
subcarrier index in 1 PRB of edge PRB
f
-f
1
2
3
4
5
6
11
12
spreading
method
a, b, c, …, f, are complex symbols

## Slide 6: SU improvement for WOLA
Using spreading method, the spectrum decay at edge band is proportional to 1/f^2, instead of 1/f (i.e. sinc-alike power decay)
Using spreading method at edge PRBs, the SU for WOLA with 2% window length can be increase up to 97.2%
No EVM issue

## Slide 7: SE improvement for WOLA (with 2% window length)
SE can be improved and always better than WOLA 50 PRB and f-OFDM with 54 PRB

## Slide 8: The spreading method can also be applied for f-OFDM on additional edge PRBs
no remarkable impact on SU and SE, while edge EVM can be improved.

## Slide 9: Complexity and latency for WOLA and f-OFDM applying spreading method
complexity: almost no added complexity
latency: no impact on latency

## Slide 10: Observations and proposal
Observations
  Using spreading method at edge PRBs can improve SU for WOLA without increasing the window length
  Using spreading method at edge PRBs does not impact on the complexity or latency
  WOLA with 2% window length can have comparable SU as f-OFDM with 50% filter length, while WOLA does not have EVM issue
  WOLA has relatively higher spectral efficiency than f-OFDM
  spreading method can also be applied for f-OFDM to reduce the edge EVM regrowth
Proposal
  RAN4 to study the implementation of spreading method at edge PRBs for the specification of minimum level of spectrum utilization.

## Slide 11: Thanks