## Slide 1: Way forward on NB-IoT absolute power tolerance
Neul, HiSilicon, Huawei

## Slide 2: Background
In current spec (36.101-d61), NB-IoT reuses the legacy LTE requirements for absolute power tolerance;
The legacy requirements assume that the DL SNR is ≥-6 dB;
As per 36.133-d60, NB-IoT UE needs to work below -6 dB (down to -15 dB) and at this SNR range, the NRSRP accuracy decreases;
New requirements for absolute power tolerance are needed in order to reflect the extended work range. Otherwise, the current requirements may not be met for UEs at low SNR (i.e. <-6 dB);
Detailed analysis in: R4-1701265

## Slide 3: Proposal
The legacy LTE absolute power tolerance requirements shall apply when the UE is with the radio condition of SNR ≥-6 dB;
For -15 ≤SNR<-6 dB, new absolute power tolerance is FFS;
An example new table is below
Conditions | Tolerance | 
 | Ês/Iot ≥ -6 dB | -15 dB ≤ Ês/Iot < -6 dB
Normal | ±9.0 dB | TBC
Extreme | ±12.0 dB | TBC
Table 6.3.5F.1-1: Absolute power tolerance