## Slide 1: Way forward on in-band requirements for NR
Agenda Item: 10.4.1.2
Document for: Approval
Source: Nokia
3GPP TSG-RAN WG4 meeting #82 Tdoc R4-1702093
Athens, Greece, 13 - 17 February, 2017

## Slide 2: Background
12 contributions discussed in agenda item 10.4.1.2
  R4-1700719 Assumptions for NR in-band emission, EVM and in-band selectivity requirements with different numerologies, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1700720 Two set of NR UE UL in-band emissions and EVM requirements for UE Tx, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1700721 NR UE Tx EVM requirements, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1700722 NR UL selectivity requirements at BS RX, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1700723 NR DL in-band EVM and emission requirements at BS TX, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1700730 NR DL in-band emission and EVM requirements at BS TX, ZTE Wistron Telecom AB
  R4-1700803 UL guard band demand due to OOBE caused by PA nonlinearity, ZTE Microelectronics Tech. Co.
  R4-1700818 TRX and PA Impairments for Multiple Numerologies in NR UL, Skyworks Solutions Inc.
  R4-1700954 In-channel Guard Band with Different Numerologies, Qualcomm Incorporated
  R4-1701158 On multi-numerology transmission and requirements, Ericsson
  R4-1701763 On EVM evaluation for multi-numerology multiplexing, ORANGE
  R4-1701889 TP for 38.803: Conclusion of NR in-band requirements, Huawei, Hisilicon
This contribution summaries the issues and agreed WF for in-band requirements

## Slide 3: Assumptions
Start evaluations of in-band performance and needed requirements for mixed numerology case by evaluating 20 MHz NR carrier with roughly two 10 MHz sub-blocks with different numerologies (15 kHz and 60 kHz SCS) for <6 GHz frequencies at the first phase
When RAN4 defines 5G NR requirements, RAN4 should ensure sufficiently good spectral efficiency in both single and mixed numerology cases
Flexibility in approach to allocating non used PRBs (guard) and filtering/windowing in order to maximize spectral efficiency for each specific link situation and different reference measurement channels e.g. with different MCSs should be enabled

## Slide 4: Assumptions
For NR mixed numerology case RAN4 should specify new type of minimum requirements to define. These might include some of the following
  how close to each other in frequency BS Tx can transmit two sub-blocks with different numerologies while still meeting the other relevant requirements like the EVM
    The possibility of several requirements with different sub-block spacing, different reference measurement channels (e.g. different MCS) and EVM may need to be considered
    Requirements should consider both the interference arising from the other numerology and impact to EVM due to filtering of a numerology
  how close to each other in frequency two sub-blocks with different numerologies could be while BS Rx and UE Rx still need to meet the relevant receiver requirements like the selectivity
    The possibility of several requirements with different sub-block spacing and selectivity may need to be considered
It is FFS how many requirements are needed for ensuring flexibility to optimize for different link situations and whether all requirements should be mandatory
  Companies should express analysis & views on which requirements are needed and whether they should be mandatory

## Slide 5: NR DL EVM and in-band emission requirements at BS TX
For single numerology case define both average BS Tx EVM requirements over all the PRBs and over 1 PRB for the edge PRBs
For mixed numerology case define both average BS Tx EVM requirements over all the PRBs of a given numerology and over 1 PRB for the edge PRBs
Consider reducing the number of test cases and testing in first phase NR specification development by defining only EVM based requirements for BS Tx in-band requirements with the mixed numerology case
Define the receiver assumptions for validating the requirements as Tx EVM measurement depends on the implementation of the receiver used for the measurement
Tx and Rx complexity should be taken into account

## Slide 6: NR UL selectivity requirements at BS RX
Define the minimum requirement for NR BS in-channel selectivity requirements with mixed numerologies as follows
  For NR, the throughput shall be ≥ TBD % of the maximum throughput of the reference measurement channel as specified in Annex TBD with parameters specified in Table TBD for NR TBD type BS
  Several requirements may need to be defined to enable flexibility to optimise the in-band approach; FFS

## Slide 7: NR UL in-band emissions and EVM requirements at UE TX
Define both average UE Tx EVM requirements measured over all the allocated PRBs and a few edge PRBs
  Study further to decide if 1 PRB EVM measurement could be assumed as narrow bandwidth UE Tx EVM measurement
TRX impairments like Image and carrier leakages and PA ACLR impact must be carefully budgeted when interference between different numerologies are studied
  TRX impairments are to be considered at any UL power levels where ACLR is only to be considered for the upper part of the UE power levels
  Need for Improved TRX impairments compared to LTE and achievable sub6GHz and mmW UE image and carrier leakage values should be further studied