## Slide 1: WF on NR subcarrier spacing and Channel bandwidth
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13th – 17th February, 2017
R4-1702096
Agenda item: 10.2
Document for: Approval

## Slide 2: Back ground (SCS)
Following SCSs are proposed in this meeting
  For sub 6GHz, 15k, 30k, and 60k are included in all companies’ proposals
  For above 6GHz, 60k, 120k and 240k are included in most companies’ proposals
R4-170xxxx | 
Qualcomm (1797) | 
Nokia (0724) | 
Ericsson (1166) | 
Huawei (1314) | 
Intel (2031) | 
2GHz
2.5GHz
3.5GHz
6GHz
24GHz
43.5GHz
52.3GHz
15k, 30k, 60k
15k, 30k, 60k
15k, 30k, 60k
15k
30k
60k
120k
240k
120k, 240k
60k, 120k, 240k, 480k (*)
* These are a set of possibilities, not proposals. Final set will depend on evaluations 480k should not be precluded at this stage.
15k, 30k, 60k
60k, 120k

## Slide 3: Back ground (CBW)
Following maximum CBWs are proposed in this meeting
R4-170xxxx | 
Qualcomm (1797) | 
Nokia (0724) | 
Samsung (1075) | 
MediaTek (1824) | 
Intel (2031) | 
2GHz
2.5GHz
3.5GHz
6GHz
24GHz
43.5GHz
52.3GHz
100M
200M
200M
20M
50M
100M
200M
400M
400M
1G
1G
100M
400M

## Slide 4: Back ground
RAN1 made following agreement in this meeting.

## Slide 5: WF on SCS
For sub 6GHz
  15kHz, 30kHz, and 60kHz are feasible SCS
  It may be that not all of these SCS are supported in every band
  In WI phase, SCSs to be specified for each band will be discussed based on the feasible SCSs.
For above 6GHz
  RAN4 has not yet reached a decision on which SCS are feasible
  60kHz, 120kHz and 240kHz are potential candidates for SCS
    Feasibility of 480kHz is FFS
  Evaluation of feasible SCS should be made based on the phase noise model(s), CBW, FFT size, service to support etc.
In WI phase, SCSs to be specified for each band will be discussed based on the feasible SCSs.
  Which of the above mentioned SCSs are supported for NR bands will be discussed in WI phase.
    SCSs mentioned above are not applicable to all bands
Note: RAN4 discussion is for common or dedicated data channel and is not applicable for special channel such as PRACH or sync channel, which is dependent on RAN1 progress.

## Slide 6: WF on CBW
For sub 6GHz
  Maximum CBW would be considered in range of 100MHz~200MHz
For above 6GHz
  Maximum CBW would be considered in range of 200MHz~1GHz400MHz1GHz
Maximum CBW to be specified will be discussed based on the above ranges in WI phase.
Maximum CBW to be supported for NR bands will be discussed in WI phase
      Maximum CBW mentioned above may be not applicable to all bands, e.g. for low frequency bands
      In case operator has spectrum higher than the maximum CBW, CA can be used to utilize whole spectrum
Subsets of CBW (e.g. 20MHz, 40MHz and so on for sub 6GHz and 80MHz, 100MHz and so on for mmWave frequency) will be discussed in WI phase.
Which CBW set is mandatory to specific UE should be according to its own transmission BW capability. How to address this issue in specification would be further studied in WI phase.

## Slide 7: WF FFT size
Based on the RAN1 agreements, the maximum FFT size should be either 4096 or 8192 in Rel-15.
For the maximum FFT size
  At least 4096 FFT size is feasible
  FFS on feasibility on of 8192 FFT size is FFS
Note: there is no mandatory on corresponding UE implementation.
Note: there is no mandate on UE and BS implementation with respect to FFT size.