## Slide 1: WF on V2V single-link tests
Huawei, HiSilicon, LGE, …
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February, 2017
Agenda Item: 7.19.4
R4-1702135

## Slide 2: Background
During RAN4 #81 meeting, we have some agreements for PSCCH and PSSCH performance requirements in [2]
  Propagation condition
    Option 1: EVA180
    Option 2: EVA1500
    Option 3: EVA2700
    Option 4: EVA1000
    Other options are not precluded and down selection in next meeting
  Relative timing error (considering Tx and Rx): 24Ts
    FFS whether to take into account V2V signal propagation delay from TX to RX. To be decided in next meeting
Channel estimation interpolation filter in time domain
  Option 1: Linear channel interpolation
  Option 2: Doppler spread conditions adaptive interpolation
  Interested companies are encouraged to provide analyses and other options are not precluded and down select in next meeting

## Slide 3: Way Forward
For PSSCH, define following test cases
  EVA180, MCS13, 20MHz, retransmission: 0 time
  EVA2700, MCS4, 10MHz, retransmission: 1 time
For PSCCH, define following test cases
  EVA1500
For joint decoding of control and data in frequency selective fading channels:
  Explicit model in simulation.
  Companies are encourages to submit results with Explicitly modelled joint decoding.

## Slide 4: Simulation assumptions
CFO and Doppler Shift Estimation Algorithm
  “Single-DMRS” estimation

## Slide 5: Reference
R4-168710, “WF on V2V demodulation performance test”, Huawei, HiSilicon, LGE, Qualcomm, Ericsson, Intel
R4-1610866, “Way forward on V2V single-link performance requirements”, Huawei, HiSilicon, LG Electronics, CATT
R4-1610701, “Way forward on V2V power imbalance tests”, LGE, Huawei, HiSilicon, Qualcomm, Ericsson, CATT, Intel