## Slide 1: WF on Demodulation Requirements for UEs Supporting Coverage Enhancements
Intel Corporation, Qualcomm, Ericsson, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February 2017
Agenda Item: 5.4.6
R4-1702164

## Slide 2: Background
The Rel-13 CE feature can be supported by any LTE UE category and not restricted to be used for Category M1 devices only
Existing UE demodulation performance and CQI requirements for the CE feature are defined based on the simulation results with the Category M1 devices with single receiver antenna
  The applicability of existing requirements for other devices with 1 RX chain is unclear
  The requirements for the devices with 2 and 4 RX chains are not defined and existing Cat M1 requirements may not be directly reused
  It is not clear how to setup the test for demodulation and CQI requirements for devices with 2 and 4 Rx chains supporting coverage enhancement.

## Slide 3: Main Session Agreements
Proposal 1: Further clarify Rel-13 CE demodulation requirements applicability for non Category M1 device categories.
Proposal 2: Define Rel-13 CE UE demodulation requirements applicability for other device types with single receive antenna.

## Slide 4: Way Forward (1)
Define Rel-13 CE UE demodulation and CQI requirements applicability for other UE types with single receive antenna:
  Existing Rel-13 CE UE demodulation requirements are applicable for “UE Category 1 + 1RX”
  FFS for “UE DL Category 0”

## Slide 5: Way Forward (2)
Define additional CE UE demodulation performance and CQI requirements for the UEs with larger number of receive chains (incl. 2 and 4 RX).
  Methodology to define the requirements for 2RX and 4RX UEs is FFS
    Option 1: Simplified antennas connection method (Ref: R4-1700875)
      Reuse the existing test setups and parameters
      The existing CE tests are performed by duplicating the fading channel from each Tx antenna and adding independent noise for each Rx antenna.
      The new CE performance requirements are introduced.
        FFS to reuse the same requirements or add some margins or similar
    Option 2: Full antenna connection method
      New CE tests with full channel models are defined under assumption that channel fading is independently generated for each RX antenna.
    Other options are not precluded
  Companies are encouraged to bring analysis on how to introduce the requirements in the RAN4 #82bis
    Example: applicable release, applicable test parameters, antenna connection methodology