## Slide 1: WF on V2V demodulation requirements
LGE, Huawei, HiSilicon, CATT
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February, 2017
Agenda Item: 7.19.4
R4-1702189

## Slide 2: Background
During RAN4 #80Bis meeting, test scope of demodulation performance tests were captured in WF[1]
  Single-link PSSCH and PSCCH demodulation performance
    Capability to handle high CFO
    Capability to handle high and low Doppler spread
    Capability of PSCCH DMRS blind detection
  Multi-link PSSCH and PSCCH demodulation performance
    Capability to perform simultaneous reception of multiple V2V links with different propagation conditions (time offset, carrier frequency error, delay spread, Doppler spread)
    Capability to perform reception of links with max power imbalance
  Maximum process test

## Slide 3: Way Forward
Remaining issues related with other WGs decision will be handled during RAN4 V2X WI phase.
Single-link performance
  Introduce new PSCCH & PSSCH performance under fading condition
    In this meeting, actual requirements can be defined with TBD
    In next meeting, actual requirements will be updated and fixed with impairment results from interesting companies
Maximum process test
  Introduce the maximum process test, the details are subjected to RAN1 decision

## Slide 4: Way Forward
Multi-link performance
  FFS whether introduce requirements for simultaneous reception of multiple V2V links with different propagation conditions or not
  Introduce new power imbalance requirement
    Define for 20MHz only
    Both UE1 and UE2 are allocated with not adjacent considering followings
      Avoid channel edge
      Avoid LO RBs
      Ensure the distance between 2 transmissions are at least 10RBs apart.
      Avoid the two transmissions being in the IQ image region of each other. (note that the IQ image is 25dBc, which is quite significant in this kind of test).
    TBC if non adjacent allocation can be used to meet all the power imbalance test case purposes
    In this meeting, SNR1 and SNR2 can be defined with [] values based on existing simulation results and further updated in next meeting with more input from interesting companies

## Slide 5: Reference
R4-168710, “WF on V2V demodulation performance test”, Huawei, HiSilicon, LGE, Qualcomm, Ericsson, Intel
R4-1610866, “Way forward on V2V single-link performance requirements”, Huawei, HiSilicon, LG Electronics, CATT
R4-1610701, “Way forward on V2V power imbalance tests”, LGE, Huawei, HiSilicon, Qualcomm, Ericsson, CATT, Intel
R4-1609763, “Discussion about maximum process tests for Rel-14 V2V,” LG Electronics
R4-1609479, “Discussion on maximum sidelink processes test for V2V”, Huawei, HiSilicon