## Slide 1: WF on Enhanced CRS-IM Performance Requirements
Intel Corporation, LGE, Ericsson
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February 2017
Agenda Item: 7.31
R4-1702195

## Slide 2: Introduction
CRS-IM enhancements work objectives:
  Stage 1: Investigate performance benefits and feasibility of using CRS-IM receivers:
  Stage 2: Specify UE demodulation and CSI reporting performance requirements to verify practical CRS-IM operation for the identified scenarios based on the outcome of Stage 1.
RAN4 #81 agreements
  R4-1610716 WF on Enhanced CRS-IM Performance Requirements
  R4-1610717 WF on simulation assumptions for Enhanced CRS-IM initial studies
This WF provides further agreements on the target scenarios and reference receivers for the Stage 1 investigations of CRS-IM enhancements and downselection of test cases for Stage 2 work
Companies are encouraged to provide further inputs on the scenarios and reference receivers performance/complexity analysis in RAN4 #82bis

## Slide 3: Enhanced CRS-IM for PDSCH (1)
Background: Candidate scenarios in RAN4 #81
Way forward:
  Confirm CRS-IM feasibility and gains for PDSCH TCs 1-4. Proceed with requirements definition for these test cases.
  Continue analysis for TC # 5-6
  TC #7 is deprioritized due to limited CRS-IC gains
Test | TM | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  |  | Serv. cell | Interf. cell
Test cases for performance requirements definition |  |  |  |  | 
1 | TM4 | Non Colliding | 2 | 4 | 4
2 | TM4 | Non Colliding | 4 | 2 | 2
3 | TM9 | Non Colliding | 4 | 2 | 2
4 | TM4 | Non Colliding | 4 | 4 | 4
Test cases for additional analysis / discussion |  |  |  |  | 
5 | TM4 | Colliding | 2 | 4 | 4
6 | TM4 | Colliding | 2 | 4 | 2
7 | TM4 | Colliding | 2 | 2 | 4

## Slide 4: Enhanced CRS-IM for PDSCH (2)
Test parameters
  Interference profile:
    TC 1-4: I1/Noc = 10.45 dB; I2/Noc = 4.6 dB; 20% RU
    TC 5-6
      Option 1: I1/Noc = 10.45 dB; I2/Noc = 4.6 dB; 20% RU
      Option 2: I1/Noc = 15.8 dB; I2/Noc = 10.5 dB; 0% RU
      Option 3: Low INR values for robustness verification (exact values TBD)
  PDSCH FRC
    Baseline for alignment: MIMO Rank 1 + 64QAM ½.
    Companies can bring inputs to further tune the MCS.
  Number of explicitly modelled interference cells
    Test 1,2,3: 2
    Test 4: 1

## Slide 5: Enhanced CRS-IM for PDCCH/PCFICH (1)
Background: Candidate scenarios in RAN4 #81
Way forward:
  Confirm CRS-IM feasibility and define requirements for TC 1.
  Deprioritize work for TC2
  Continue studies for additional PDCCH/PCFICH TC3 (investigate both performance and complexity).
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
1 | Non Colliding | 2 | 4 | 4
2 | Non Colliding | 4 | 2 | 2
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
3 | Non Colliding | 4 | 4 | 4

## Slide 6: Enhanced CRS-IM for PDCCH/PCFICH (2)
Interference power profile:
  I1/Noc = 13.91 dB; I2/Noc = 3.34 dB (Rel-13 CCIM)
PDCCH parameters
  Test #1: CFI = 2; PDCCH AL 2
  Test #3: CFI = 2; PDCCH AL [1, 2]

## Slide 7: Enhanced CRS-IM PHICH
Background: Candidate scenarios in RAN4 #81
Way forward:
  Confirm performance gains for PHICH TC 1. FFS if performance requirements need to be introduced.
  Deprioritize work for TC2
  Continue studies for additional PHICH TC3 (investigate both performance and complexity).
Interference profile: I1/Noc = 13.91 dB; I2/Noc = 3.34 dB (Rel-13 CCIM)
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
1 | Non Colliding | 2 | 4 | 4
2 | Non Colliding | 4 | 2 | 2
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
3 | Non Colliding | 4 | 4 | 4

## Slide 8: Enhanced CRS-IM for EPDCCH
Stage 1 analysis confirms CRS-IM performance gains for the evaluated EPDCCH scenarios
Work on the Enhanced CRS-IM performance requirements for EPDCCH is deprioritized
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
1 | Non Colliding | 4 | 2 | 2

## Slide 9: Other test parameters
Explicitly model 1 interference cell for scenarios with 4RX antennas and 4 CRS APs in the interference cells scenarios

## Slide 10: Reference Receivers
CRS-IM receivers for 4 CRS APs ports processing
  Do not specify the exact receiver type (full/reduced complexity) for the minimum requirements definition
CRS-IM receivers for colliding CRS
  Further bring analysis on the performance/complexity for the following colliding CRS-IM reference receivers for test #5
    CRS-IM Receiver #1: LMMSE-IRC with 1 Cell CRS-IM to improve channel estimation
    CRS-IM Receiver #2: LMMSE-IRC with 1 Cell CRS-IM to improve channel and interference estimation
  Further bring analysis on the performance/complexity for the following colliding CRS-IM reference receivers for test #6
    CRS-IM Receiver #1: LMMSE-IRC with covariance matrix estimation on serving cell APs 0-3 + 1 Cell CRS-IM
    CRS-IM Receiver #2: LMMSE-IRC with covariance matrix estimation on serving cell APs 2-3+ 1 Cell CRS-IM

## Slide 11: UE Capabilities/Features
Further discuss Enhanced CRS-IM UE features and capability signalling
UE features (capabilities) for CRS-IM
  FFS whether to define separate capabilities for 2RX and 4RX CRS-IM
  Data and control channels
    Option 1: Define separate CRS-IM capabilities for PDSCH and DL Control channels
    Option 2: Do not differentiate between PDSCH and DL Control channels CRS-IM capabilities
  Number of CRS APs
    Option 1: Define separate capabilities for CRS-IM for 1/2 and 4 CRS APs. 2 CRS APs capability is a pre-requisite for the 4 CRS APs capability.
    Option 2: Do not differentiate between 2 and 4 ports CRS-IM capabilities

## Slide 12: UE Capabilities/Features
Capability signalling
  Option 1: Define per-UE capability signalling for each feature:
    Indicate support of CRS-IM on at least one CC.
    FFS if any constrains on the max CC CA configuration should be signaled.
  Other options are not precluded

## Slide 13: Summary of CRS-IM alignment results for PDSCH in RAN4 #82 (for information)
Test | TM | CRS pattern | Number of UE RX chains | Number of CRS APs |  | Modulation | CRS-IM SINR, dB | CRS-IM gain vs IRC, dB
 |  |  |  | Serv. cell | Interf. cell |  |  | 
Test 1-1 | TM4 | Non Colliding | 2 | 4 | 4 | 16QAM | -4.7 | 2.6
Test 1-2 |  |  |  |  |  | 64QAM | 0.5 | 2.0
Test 2-1 | TM4 | Non Colliding | 4 | 2 | 2 | 16QAM | -6.4 | 2.5
Test 2-2 |  |  |  |  |  | 64QAM | -2.8 | 2.3
Test 3-1 | TM9 | Non Colliding | 4 | 2 | 2 | 16QAM | -6.2 | 2.3
Test 3-2 |  |  |  |  |  | 64QAM | -2.0 | 1.8
Test 4-1 | TM4 | Non Colliding | 4 | 4 | 4 | 16QAM | -7.6 | 2.9
Test 4-2 |  |  |  |  |  | 64QAM | -3.1 | 2.4
Test 5-1 | TM4 | Colliding | 2 | 4 | 4 | 16QAM | -3.8 | 1.2
Test 5-2 |  |  |  |  |  | 64QAM | 0.4 | 1.3
Test 6-1 | TM4 | Colliding | 2 | 4 | 2 | 16QAM | -5.3 | 1.4
Test 6-2 |  |  |  |  |  | 64QAM | -1.0 | 1.8
Test 7-1 | TM4 | Colliding | 2 | 2 | 4 | 16QAM | -0.7 | 1.1
Test 7-2 |  |  |  |  |  | 64QAM | 2.2 | 1.0
Note: Results are based on R4-1702193

## Slide 14: Summary of CRS-IM alignment results for DL Control Channels in RAN4 #82 (for information)
Test | CRS pattern | Number of UE RX chains | Number of CRS APs |  | Interf. Model | CFI | INR1, INR2 | SINR CRS-IM, dB | CRS-IM gain vs MRC, dB | CRS-IM gain vs IRC, dB
 |  |  | Serv. cell | Interf. cell |  |  |  |  |  | 
PDCCH test 1-1 | Non Colliding | 2 | 4 | 4 | Rel-13 CCIM (TS 36.101 B.7) | 2 | 13.91, 3.34 | -2.5 | 2.7 | 2.3
PDCCH test 1-2 |  |  |  |  |  |  | 8.36, 1.66 | -1.9 | 2.0 | 1.6
PDCCH test 1-3 |  |  |  |  |  | 3 | 13.91, 3.34 | -2.0 | 1.8 | 1.3
PDCCH test 1-4 |  |  |  |  |  |  | 8.36, 1.66 | -1.7 | 1.5 | 1.0
PDCCH test 2-1 | Non Colliding | 4 | 2 | 2 |  | 1 | 13.91, 3.34 | -9.1 | 6.0 | 2.1
PDCCH test 2-2 |  |  |  |  |  |  | 8.36, 1.66 | -7.1 | 3.8 | 1.5
PDCCH test 2-3 |  |  |  |  |  | 3 | 13.91, 3.34 | -7.5 | 4.1 | 0.4
PDCCH test 2-4 |  |  |  |  |  |  | 8.36, 1.66 | -6.1 | 2.9 | 0.2
PHICH test 1-1 | Non-Colliding | 2 | 4 | 4 |  | 3 | 13.91, 3.34 | -1.9 | 1.7 | 1.3
PHICH test 1-2 |  |  |  |  |  |  | 8.36, 1.66 | -2.1 | 1.3 | 0.9
PHICH test 2-1 | Non-Colliding | 4 | 2 | 2 |  | 1 | 13.91, 3.34 | -8.4 | 5.5 | 1.8
PHICH test 2-2 |  |  |  |  |  |  | 8.36, 1.66 | -6.7 | 3.8 | 1.4
EPDCCH test 1-1 | Non-Colliding | 4 | 2 | 2 | Model #1 | 1 | 13.91, 3.34 | -10.1 | 5.1 | 5.5
EPDCCH test 1-2 | Non-Colliding | 4 | 2 | 2 | Model #2 |  | 10.44, 4.57 | -5.8 | 6.3 | 2.3
EPDCCH test 1-3 | Non-Colliding | 4 | 2 | 2 | Model #3 |  | 8.36, 1.66 | -3.0 | 5.2 | 1.2
Note: Results are based on R4-1702194