## Slide 1: WF on MUST performance tests
MediaTek
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13th - 17th February 2017
Agenda Item: 7.28.1
R4-1702303

## Slide 2: Way Forward
MUST Case 1 and Case 2
  No new test on far UE decoding performance
  No new test for starting OFDM symbol
  No new test on PDCCH decoding performance
  Introducing following 3 test cases for MUST Case 1 and Case 2
    Test A1: TM2, 64QAM, with p-a-must. Both UEs are rank-1
    Test A2: TM3, QPSK, without p-a-must. Both UEs are rank-2
    Test A3: TM4, 16QAM without p-a-must. MUST-near UEs is rank-2, and MUST-far UE is rank-1
  Assumption of DL Tx EVM for evaluation: 6%

## Slide 3: Way Forward
MUST Case 1 and Case 2
  Companies are encouraged to provide views on the following parameters
    MCS level
    Exact values of p-a and p-a-must
    Random or fix power ratio

## Slide 4: Way Forward
MUST Case 3
  Introducing the following 3 test cases for MUST Case 3
    Test B1: TM8 or 9, dmrs-tableAlt = 0, k-max =1, BMUST = 2, 2Rx
    Test B2: TM9 or 10, dmrs-tableAlt = 1, k-max =1, BMUST = 4, 2Rx
    Test B3: TM9 or 10, dmrs-tableAlt = 1, k-max =3, BMUST = 6, 4Rx
    where BMUST is the number of additional bits added in the extended DCI formats
  Rank of target UE is 1 for all tests
  R-ML as the reference receiver to specify tests

## Slide 5: Way Forward
MUST Case 3
  Companies are encouraged to provide views on the following parameters
    Tx antenna number
    TM
    MCS level
    Interference modulation level
    Precoder assumption
    The number of interference layers in Test B3.

## Slide 6: For information
Simulation assumptions for MUST Case 1 and Case 2
Parameter | Unit | Value
Bandwidth | MHz | 10
Duplex mode |  | FDD
Cyclic Prefix |  | Normal
Cell_ID |  | 0
 | dB | -3
 | dB | -3
 | dB | 0
Cell-specific reference signals |  | Antenna ports 0,1
Propagation Condition |  | EVA5
Correlation Matrix and Antenna Configuration |  | 2x2 Low
Subframe # with PDSCH |  | #1, 2, 3, 4, 6, 7, 8, 9
Number of HARQ processes per component carrier | Processes | 8
Maximum number of HARQ transmission |  | 4
Redundancy version coding sequence |  | {0,1,2,3} for QPSK and 16QAM {0,0,1,2} for 64QAM
Number of OFDM symbols for PDCCH | OFDM symbols | 2
Demapper algorithm for decoupling spatial layers |  | MMSE or others
Demapper algorithm for calculating LLR within a layer |  | R-ML

## Slide 7: For information
Simulation assumptions for MUST Case 3
Parameter | Unit | Value
Bandwidth | MHz | 10
Duplex mode |  | FDD
Cyclic Prefix |  | Normal
Cell_ID |  | 0
 | dB | 0
 | dB | 0
 | dB | -3
Cell-specific reference signals |  | Antenna ports 0,1
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS | Subframes | 5 / 2
CSI reference signal configuration |  | 3
Zero-power CSI-RS configuration ICSI-RS / ZeroPowerCSI-RS bitmap | Subframes / bitmap | 3 / 0001000000000000
Propagation Condition |  | EPA5
Subframe # with PDSCH |  | #0, 1, 2, 3, 4, 6, 7, 8, 9
Reference channel |  | R.50 FDD
Number of HARQ processes per component carrier | Processes | 8
Maximum number of HARQ transmission |  | 4
Redundancy version coding sequence |  | {0,0,1,2}
Number of OFDM symbols for PDCCH | OFDM symbols | 2