## Slide 1: WF on MUST performance tests
MediaTek
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13th - 17th February 2017
Agenda Item: 7.28.1
R4-1702309

## Slide 2: Way Forward
MUST Case 1 and Case 2
  No new test on far UE decoding performance
  No new test for starting OFDM symbol
  No new test on PDCCH decoding performance
  Introduce test cases to cover
    Transmission modes:
      TM2 and TM4
      TM3 is FFS
    Near UE modulation levels:
      QPSK, 16QAM
      FFS on the feasibility of 64QAM under EVM 6%.
    Different rank combinations of near and far UEs
      Option 1: Both rank-1
      Option 2: Both rank-2
      Option 3: Near UE rank-2 and far UE rank-1
    With and without p-a-must configuration

## Slide 3: Way Forward
MUST Case 1 and Case 2
  Companies are also encouraged to provide views on the following parameters
    MCS level
    Exact values of p-a and p-a-must
    Random or fix power ratio

## Slide 4: Way Forward
MUST Case 3
  Investigate the following 3 scenarios for MUST Case 3
    Test B1: TM9, dmrs-tableAlt = 0, k-max =1, BMUST = 2, 2Rx
    Test B2: TM9, dmrs-tableAlt = 1, k-max =1, BMUST = 4, 2Rx
    Test B3: TM9, dmrs-tableAlt = 1, k-max =3, BMUST = 6, 4Rx
    where BMUST is the number of additional bits added in the extended DCI formatsRank of target UE is 1 for all tests
  Working assumption for Investigation: R-ML as the reference receiver

## Slide 5: Way Forward
MUST Case 3
  Companies are also encouraged to provide views on the following parameters
    Tx antenna number
    Rx antenna number
    MCS level
    Interference modulation level
    Precoder assumption
    The number of interference layers in Test B3.
    OCC (OCC2, OCC4)

## Slide 6: For information
Simulation assumptions for MUST Case 1 and Case 2
Parameter | Unit | Value
Bandwidth | MHz | 10
Duplex mode |  | FDD
Cyclic Prefix |  | Normal
Cell_ID |  | 0
 | dB | -3
 | dB | -3
 | dB | 0
Cell-specific reference signals |  | Antenna ports 0,1
Propagation Condition |  | EVA5
Correlation Matrix and Antenna Configuration |  | 2x2 Low
Subframe # with PDSCH |  | #1, 2, 3, 4, 6, 7, 8, 9
Number of HARQ processes per component carrier | Processes | 8
Maximum number of HARQ transmission |  | 4
Redundancy version coding sequence |  | {0,1,2,3} for QPSK and 16QAM {0,0,1,2} for 64QAM
Number of OFDM symbols for PDCCH | OFDM symbols | 2
Demapper algorithm for decoupling spatial layers |  | MMSE or others
Demapper algorithm for calculating LLR within a layer |  | R-ML

## Slide 7: For information
Simulation assumptions for MUST Case 3
Parameter | Unit | Value
Bandwidth | MHz | 10
Duplex mode |  | FDD
Cyclic Prefix |  | Normal
Cell_ID |  | 0
 | dB | 0
 | dB | 0
 | dB | -3
Cell-specific reference signals |  | Antenna ports 0,1
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS | Subframes | 5 / 2
CSI reference signal configuration |  | 3
Zero-power CSI-RS configuration ICSI-RS / ZeroPowerCSI-RS bitmap | Subframes / bitmap | 3 / 0001000000000000
Propagation Condition |  | EPA5
Subframe # with PDSCH |  | #0, 1, 2, 3, 4, 6, 7, 8, 9
Reference channel |  | R.50 FDD
Number of HARQ processes per component carrier | Processes | 8
Maximum number of HARQ transmission |  | 4
Redundancy version coding sequence |  | {0,1,2,3} for QPSK and 16QAM {0,0,1,2} for 64QAM
Number of OFDM symbols for PDCCH | OFDM symbols | 2