## Slide 1: WF on RRM Requirements for UE Capable of Coverage Enhancement
Ericsson, Qualcomm, Nokia, Alcatel-Lucent Shanghai Bell, Huawei, HiSilicon, Intel….
3GPP TSG-RAN WG4 Meeting #82 Athens, Greece, 13 - 17 February 2017
Agenda Item: 5.4.3
R4-1702326

## Slide 2: Background
The LTE coverage enhancement (CE) feature can be supported by any Rel-13 LTE UE category Legacy (UE Cat-L).
  UE Cat-L supports 2 Rx or 4 Rx.
The existing Rel-13 RRM requirements defined for CE (i.e. CE Mode B) are applicable only for UE category M1.
There are no RRM requirements specified for UE Cat-L which supports CE.
Note: UE Cat-L: All Rel-13 UE categories except UE category 0 and UE category M1.

## Slide 3: Agreements
RAN4 shall specify RRM requirements for all UE Cat-L supporting CE in Rel-13.
With the exception of the RRM requirements listed below, existing RRM requirements defined for UE cat-M1 in Rel-13 can be reused for UE Cat-L according to its CE Mode capability:
  Radio link monitoring (RLM),
  SI acquisition time i.e. requirements involving time to acquire MIB and/or SIB1-BR
  RSRP and RSRQ measurement accuracies
RAN4 is to further investigate the above requirements under CE for UE Cat-L assuming 2Rx i.e.
  RLM,
  SI acquisition time (i.e. MIB and/or SIB1-BR)
  RSRP/RSRQ accuracies
Timeline:
  Interested companies are expected to provide analysis and results in RAN4#82bis.
  Specify RRM requirements by RAN4#83 subject to the completion of analysis.